## Slide 1: Does Future Home Networking Look Blue?
David Cypher
Information Technology Laboratory

## Slide 2: Devices in the home
Anything that runs on electricity
  Obvious
    telephones
    personal computer(s)
    televisions
    VCR
    CD- & DVD-players
    stereo/radio
    security system & sensors
  Not-so obvious
    door bell
    clocks
    garage door
    lights
    heating & air conditioning
    washer/dryer
    kitchen appliances

## Slide 3: Why connect devices in the home
Cable replacement
Lack of access
Movement
Centralize control (remote control)
Sharing data
New services or functions

## Slide 4: What devices to connect in the home
Hand set to Cradle
Cradle to Access Point
Keyboard, Mouse, Monitor, Printer, etc. to Personal Computer
PC to PC
Televisions to remote or signal receiver (i.e antenna, cable, satellite)
Clocks
On/Off button to bell, lights, garage door, etc.
Alarms or indications to single point (i.e. human or control panel)
CD- & DVD-players and stereo/radio to remotes, head sets, and speakers

## Slide 5: How to connect devices in the home
Cables (Coax, Twisted pair, other)
Telephone wiring (HomePNA)
Wireless (HomeRF & Bluetooth)

## Slide 6: HomePNA
HomePNA 2.0
  Data rate
    10 Mbit/s
  Over existing phone wires
HomePNA 1.0
  Data rate
    1 Mbit/s
  Over existing phone wires

## Slide 7: HomeRF
SWAP 1.0 ($500.00)
  Multiplexing scheme
    TDMA &
    CDMA/CA
  Data rates
    0.8 Mbit/s
    1.6 Mbit/s
  Voice
    32 K ADPCM
    4 connections
  Distance
    100 meters
SWAP 2.0 ($2500.00)
  Multiplexing schemes
    TDMA,
    CDMA/CA, &
    Priority CDMA
  Data rates
    5 Mbit/s
    10 Mbit/s
  Voice
    32 K ADPCM
    8 connections

## Slide 8: HomeRF

## Slide 9: Bluetooth
Core 1.0, 1.0A, 1.0B, & 1.1 (free)
  Multiplexing scheme
    TDMA
  Data Rate
    433.9 kbit/s max symmetric
    723.2 kbit/s max asymmetric
  Voice
    64 kbit/s
    1,2, or 3 connections
  Distance
    10 meters

## Slide 10: Bluetooth protocols (core)
Radio
Baseband
Link Manager Protocol (LMP)
Logical Link Control and Adaptation Protocol (L2CAP)
Host Control Interface (HCI)
Service Discovery Protocol (SDP)
RFCOMM
IrDA Interoperability
Telephony Control Protocol (TCP)
Test Mode

## Slide 11: Bluetooth (piconet)
Piconet
  ACL
    (1 Master & 1-7 Slaves)
  SCO
    (1 Master & 1-3 Slaves)
  Mixed
    (1 Master & 1-* Slaves)

## Slide 12: Bluetooth (scatternet)
Scatternet
  ACL
    (2 Masters & ????)
  SCO
    (2 Masters & 1 Slave using HV3)

## Slide 13: Performance tests
Various Baseband packet types used
1, 3, and 10 meter distances used
Developers’ kit used
Various environments used

## Slide 14: Performance data (hallway)
No significant difference whether Master or Slave
3 meter distance appears to have lowest average packet loss
No significant Packet loss difference as distances change

## Slide 15: Performance data (with microwave)
Significant impact at only 1 meter distance between Master and Slave devices

## Slide 16: Performance data (country)
Could not reach 10 meters, only 8.36 meters
Significant error differences with change in distance

## Slide 17: Applicability of technologies to home devices

## Slide 18: Applicability of technologies to home devices

## Slide 19: Applicability of technologies to home devices