Reconciliation of Experimental and Computed Thermodynamic Properties for Methyl-Substituted 3-Ring Aromatics. Part 2: 3Methylphenanthrene

Andrei Kazakov,* Eugene Paulechka, and Robert D. Chirico

Thermodynamics Research Center, Applied Chemicals and Materials Division, National Institute of Standards and Technology, Boulder, CO 80305-3337, U.S.A.

* Corresponding author. E-mail address: andrei.kazakov@nist.gov

Abstract

Measurements leading to the calculation of thermodynamic properties in the ideal-gas state for 3-methylphenanthrene (Chemical Abstracts registry number [832-71-3]) are reported. Experimental methods were adiabatic heat-capacity calorimetry, differential scanning calorimetry (d.s.c.), comparative ebulliometry, inclined-piston manometry, vibrating-tube densitometry, and oxygen bomb calorimetry. The critical temperature, critical pressure, and critical density were estimated based on these measurements. Molar thermodynamic functions for the condensed and ideal-gas states were derived from the experimental results. Statistical calculations were performed based on molecular geometry optimization and vibrational frequencies using B3LYP hybrid density functional theory with the def2-QZVPD basis set. Differences between computed and experimentally derived ideal-gas entropies are larger than the experimental uncertainties, but good accord is achieved if the two lowest-frequencies vibrational modes are assumed to be coupled, as was found for 9-methylanthracene in Part 1 of this pair of articles. The enthalpy of formation for 3-methylphenanthrene in the ideal-gas phase was computed with an atom-equivalent based protocol described recently, and excellent agreement with the experimental value is shown. Experimental results are compared with literature values, where possible.

1. Introduction

This article is the second in a pair concerning reconciliation of thermodynamic properties for three-ring methyl-substituted aromatics measured experimentally and calculated with the methods of computational chemistry. This work is part of our continuing research into quantification of uncertainties for thermodynamic properties derived with computational methods.- In the previous article (Part 11), we showed that consideration of coupled non-harmonic molecular vibrations in the computations was essential in reconciling the experimental and computational results for 9-methylanthracene (abbreviated “9MA”). In that case, Nakagaki et al., had studied the coupling through fluorescence spectra of 9MA measured in a free supersonic jet expansion, and their results were used to compute energy levels for the coupled vibrational modes. Analogous experiments have not been reported for 3methylphenanthrene (abbreviated “3MP”), but, based on comparisons of experimental and computed results, we are able to show evidence for a similar coupling in 3MP.

Table 1 provides a summary of all property measurements reported here for 3MP. Entropies for a wide range of temperatures (298.15 ≤ T/K ≤ 700) and the enthalpy of formation at T/K = 298.15, both for the ideal-gas state, were derived from the results, and these are compared with independently computed values. Excellent accord will be shown between the experimental and computed ideal-gas enthalpy of formation for 3MP. Full accord between experimental and computed ideal-gas entropies was achieved only with the assumption that the two lowest-wavenumber vibrations were coupled, as seen for 9MA.1,13 Results here do not prove that such coupling exists, but we hypothesize its existence through analogy with the 9MA results. Few reports of physical properties for 3MP are available in the literature, but comparisons are made with the present results, where possible.

2. EXPERIMENTAL SECTION

2.1 Materials. The sample of 3-methylphenanthrene (abbreviated “3MP”) was synthesized and purified by the research group of Professor E. J. “Pete” Eisenbraun of Oklahoma State University in the late 1980s. Description of the synthesis route is included as Supporting Information. The mole fraction purity x = 0.9997 was determined by fractional melting in an adiabatic calorimeter, as described later in section 3.1.

Sources of reference materials (water and decane) used in the ebulliometric vapor-pressure measurements have been described. All samples were transferred under nitrogen or helium or by vacuum distillation.

2.2. Physical constants and standards. The molar mass used for 3MP was M = 192.255 gmol1 based on the formula C15H12 and the midpoints of the ranges for the standard atomic weights published by the International Union of Pure and Applied Chemistry (IUPAC). The gas constant R = 8.314462618 J.K1.mol1, the speed of light in vacuum c = 299792458 ms–1, and the Planck constant h =6.6260701510–34 JHz–1 adopted by CODATA are used. The gas constant is rounded here to R = 8.31446 J.K1.mol1 in all tables. Other calibrations are as described in section 2.2 of Part 1.1 Mass, time, electrical resistance, and potential difference were measured in terms of standards traceable to calibrations at NIST.

2.3. Adiabatic heat-capacity calorimetry. Heat-capacities and enthalpy increments for the condensed phases of 3MP were measured in the temperature range (6 < T/K < 520) with an adiabatic calorimetric system that has been described. The enthalpy of melting, triple-point temperature Ttp, and sample purity were determined in measurements with this apparatus. No solid-to-solid phase transitions were detected. Details of the sample and experimental conditions are given in Table 2. Energy increments to the filled calorimeter were corrected for enthalpy changes in the empty calorimeter, presence of the helium exchange gas, and for vaporization of the sample into the free space of the sealed container. Maximum sizes of these adjustments are included in Table 2.

2.4. Differential scanning calorimetry. Heat capacities at vapor-saturation pressure Csat,m for the liquid phase in the temperature range (355 < T/K < 755) were determined with a differential scanning calorimeter (d.s.c.). The method and apparatus were the same as that described in section 2.4 of Part 1.1 As was found for 9MA, determination of the critical temperature Tc for 3MP with d.s.c. was not possible due to sample decomposition. The value of Tc for 3MP used in this research was estimated, as described later.

2.5. Comparative ebulliometry. The method for determination of vapor pressures with comparative ebulliometry has been described., A sample of 3MP was refluxed with standards of known vapor pressure (decane for 2 < p/kPa < 25 and water for 25 < p/kPa < 270) under a common atmosphere of helium gas. Data sources for the standards and details of the uncertainty calculations for the vapor pressures were provided in Part 1.1

2.6. Inclined-piston manometry. Vapor pressures for 3MP were measured with the inclined-piston apparatus described in section 2.6 of Part 1.1 Details of the uncertainty assessment are provided there.

2.7 Densitometry. Densities at vapor saturation pressure sat were measured for 3MP with a vibrating-tube densitometer with a standard uncertainty u(sat) = 1·103sat based on comparison with reliable literature values, as described in section 2.7 of Part 1.1

2.8. Combustion calorimetry. Procedures, used in the combustion calorimetry of organic C,H,O,N containing compounds, have been described., A rotating-bomb calorimeter (laboratory designation BMR II) and platinum-lined bomb (laboratory designation B57-I) with an internal volume of 0.3930 dm3 were used without rotation. Samples (~0.9 g) of 3MP were burned as compressed pellets. Additional experimental details were the same as for 9MA and are given in section 2.8 of Part 1.1

NIST Standard Reference Material benzoic acid (sample 39i), was used for calibration of the combustion calorimeter, also as described in Part 1.1 The energy equivalent (calor) of the calorimeter was determined to be (16641.6 ± 0.7) J∙K1 (mean and standard deviation of the mean for six combustions). For the cotton fuse, empirical formula CH1.774O0.887, cU/Mwas 16945 Jg1.23

The density of the crystal phase of 3MP at T = 298.15 K and p = 0.1 MPa was estimated to be 1224 kg.m3, as was the value 2.65∙108 m3∙K1 for (∂Vm/∂T)p. The density of the crystal phase was estimated to be 12 percent greater than that of the liquid at T/K = 298.15 which was itself estimated by extrapolation of density values measured in this research with the Riedel equation, as given later in section 3.3. The value of (∂Vm/∂T)p is based on a recent literature review of thermal expansion properties for organic crystals. The molar heat capacity of the crystals at T/K = 298.15 was measured with adiabatic calorimetry in this research and is reported later in this article. These values are required for reducing apparent mass to mass, converting the energy of the actual bomb process to that of the isothermal process, and reduction to standard states.,

Carbon dioxide was recovered from the combustion products of each experiment. The method has been described. No evidence of incomplete combustion was detected. The weight percent recoveries of carbon dioxide were {(100.001 ± 0.005) mean and standard deviation of the mean} for the six combustions of benzoic acid and (99.997 ± 0.004) for 3MP.

2.9 Computation of properties for the ideal-gas state. Computational models used for generation of ideal-gas properties for 3MP are the same as those used for 9MA,1 which, in turn, are based on our previous study. Optimization of geometries and calculation of vibrational frequencies were performed using B3LYP hybrid density functional theory with the def2-QZVPD basis set. The scaling factors for vibrational frequencies were 0.9601 for hydrogen stretches and 0.9689 for all others, as optimized previously27 for the ideal-gas entropies of aromatics.

As previously,1 additional calculations were made for evaluation of the small methyl torsion barrier. These were performed using B3LYP, the density-fitted implementation of second-order Møller-Plesset perturbation theory (DF-MP2), and the local coupled-cluster LCCSD(T) implementation of Kállay et al. (2016 version)., DF-MP2 and LCCSD(T) calculations were performed with Dunning’s correlation-consistent aug-cc-pVXZ (X=Q,5) basis sets.

Contributions of the two lowest-frequency modes involving the methyl torsion were computed with two models; (1) with one mode treated as a free methyl rotor and the second as a harmonic oscillator (the “free-rotor” model), and (2) with a 2-dimensional model based on coupling of the two lowest-frequency modes (the “2-D” model).1,13 Justification for use of this 2-D model is provided later in Section 4.1 and 4.2. As discussed later, the torsional barrier to methyl rotation in 3MP is small (i.e., less than 2 kJmol1) and, at the temperatures of interest to this study (298.15 ≤ T/K ≤ 700), the hindrance effect on the computed entropies is negligible and a simple free-rotor model can be used. This was demonstrated previously for 9MA in Supporting Information for Part 1,1 and results for 3MP are closely analogous. Ideal-gas entropies for 3MP computed with the free-rotor and 2-D models are compared with those derived from the experimental property measurements later in section 4.7.

B3LYP calculations were done with Gaussian 16 with “tight” optimization criteria and “ultrafine” DFT integration grid. DF-MP2 calculations were performed with Psi4 v.1.3.2,, also with “tight” optimization criteria. Single-point energy LCCSD(T) calculations were carried out with MRCC (releases of February 9, 2019 and February 22, 2020) with the “tight” setting selected for local thresholds.

2.10. Computation of the enthalpy of formation for the ideal-gas state. The enthalpy of formation for 3MP was computed with the “aLL5” protocol described by Paulechka and Kazakov. The total energies were calculated at the LCCSD(T)/aug-cc-pVQZ//DF-MP2/ aug-cc-pVQZ theory level using MRCC,34 and the vibrational frequencies were computed at the B3LYP-D3(BJ)/def2-TZVP theory level. For the thermal enthalpy calculations, the frequencies scaled by the factors of 0.96 for hydrogen stretches and 0.985 for all other modes; for zero-point vibrational energy (ZPVE), a single scaling factor of 0.990 was used.35

3. Experimental Results

3.1 Heat capacities and properties of melting determined with adiabatic calorimetry. Crystals of 3MP were prepared by slow cooling (~1 mKs1) the sample to ~15 K below Ttp, where crystallization began. The sample was subsequently cooled slowly to 60 K below Ttp and reheated into the partially melted state (~20 percent liquid) under adiabatic conditions. The sample warmed spontaneously for approximately 36 h as ordering of the crystals progressed. The sample was, then, cooled at an effective rate of 1 mK·s1 to crystallize the remaining liquid. The sample was thermally cycled from temperatures T/K ≈ 265 to within 3 K of Ttp, where it was held for ~24 h to provide further tempering, during which time the sample warmed slowly for approximately the first 4 h. No further warming was observed during any of the measurements following this treatment. All results for the solid-phase were performed on crystals pre-treated with this method, and good repeatability (within 0.001Δ) was observed for the enthalpy of melting Δ.

The triple-point temperature Ttp and the mole fraction purity x were determined by measurement of the equilibrium melting temperatures T(F) as a function of fraction F of the sample in the liquid state, as described for 9MA in Part 1.1 The observed equilibrium temperatures and fractions melted F are given in Table 3, together with the derived purity and Ttp.

Measured molar enthalpy increments for 3MP are given in Table 4. Results for single-phase regions serve as checks of consistency against the integrated molar heat-capacity values. The large number of measurements in the crystal phase were carried out to ensure that no problems with the measurement system resulted from repair of an electrical short in an adiabatic shield heater. In the final column of Table 4 it can be see that agreement is within 0.1 percent for all measurements. Corrections for pre-melting caused by impurities were made. Results with the same series number N in Tables 4 and 5 were taken in sequence without interruption of adiabatic conditions.

Equilibrium was reached in less than 1 h for all measurements in the liquid phase, as well as in the solid phase for measurements more than 50 K below Ttp. Equilibration times increased to approximately 12 h within 5 K of Ttp. This general behavior is common for organic compounds near Ttp in the solid state.

Molar heat capacities under vapor saturation pressure Csat,m determined by adiabatic calorimetry for 3MP are listed in Table 5 and shown in Fig. 1. Values in Table 5 were corrected for pre-melting and the effects of sample vaporization into the gas space of the calorimeter, although the size of this correction is very small (Table 2). Due to the purity of the sample, pre-melting corrections were also small, with a maximum correction of ~0.01Csat near T/K = 325 and falling rapidly to less than ~0.001Csat near T/K = 300 K (~35 K below Ttp). Extrapolation of the heat-capacity results to T0 K was made with a plot of Csat/T against T2 for temperatures T < 10 K.

3.2. Vapor pressures

Experimental vapor pressures for 3MP are listed in Table 6. The upper pressure limit of the ebulliometer (p = 270 kPa), was reached in these measurements; however, some sample degradation is evidenced at the highest temperature (T/K = 633), where the difference between the boiling and condensation temperatures of the sample (T/K of Table 6) increases sharply from near 0.001 K at T/K = 614 to 0.02 K at T/K = 633.

The Wagner equation in the following form was used to represent the vapor pressures:

ln(p/pc) = (1/Tr){A(1–Tr) + B(1–Tr)1.5 + C(1–Tr)2.5 + D(1–Tr)4.5},	(1)

where Tc and pc are the critical temperature and critical pressure, and Tr = T/Tc. This form (abbreviated “1.5/2.5/4.5”, where the numbers represent the equation exponents) was chosen to provide optimum extrapolation to temperatures below the range of the measurements, as discussed later in Section 4.3. Tc was estimated with the method of Joback,, and pc were estimated as described for 9MA in section 3.2 of Part 1.1 The fitted parameters and estimated critical constants are listed in Table 7. The range of applicability for the equation is (298.15 ≤ T/K ≤ 700).

3.3. Densities. Experimental densities for 3MP at vapor-saturation pressure sat are listed in table 8. Minimization of deviations of the experimental values from the extended corresponding-states equation (eq 2) of Riedel,  as formulated by Hales and Townsend,  was used to evaluate the critical density, together with the acentric factor evaluated in this research.

c = 1.0 + 0.85(1 – Tr) + (1.6916 + 0.9846)(1 – Tr)1/3,	(2)

where Tr is the reduced temperature T/Tc. Relative deviations of the correlation from the experimental density values are included in table 8.

3.4 Derived Enthalpies of Vaporization. Molar enthalpies of vaporization  were calculated for 3MP with the Clapeyron equation and 2nd and 3rd virial coefficients estimated with corresponding-states correlations, , as described in section 3.4 of Part 1.1 Derived molar enthalpies of vaporization are listed in Table 9. Relative standard uncertainties for the second and third virial coefficients were estimated to be 10 percent of the estimated value, and these are the dominant contributions to the uncertainties in the derived enthalpies of vaporization for p > 0.1 MPa.

3.5. Heat capacities for the liquid phase measured with d.s.c. Two-phase (liquid + gas) heat capacities for 3MP were measured with d.s.c for three cell fillings in the temperature range (355 < T/K < 715) and are given in Table 10. Sample decomposition precluded measurements at higher temperatures. Some sample decomposition was noted in the ebulliometric vapor-pressure measurements near T/K = 633. It was possible to obtain measurements to T/K = 715 with d.s.c. because of the relative speed of the measurements.

Calculation of Csat,m values from the measured values has been described., Required vapor pressures and densities for the liquid phase were calculated with the Wagner equation (eq 1) and the corresponding states correlation given in section 3.3 of Part 1.1 Parameters for these equations are given in Table 7. A polynomial was fit to the liquid-phase heat capacities derived from the d.s.c. results together with values of Csat,m determined with adiabatic calorimetry for the temperature range 450 < (T/K) < 520 with appropriate weighting based on the uncertainties. Values of Csat,m derived with these methods are given in the last two columns of Table 10. The measurements with d.s.c. allowed extension of the heat-capacity results from T = 520 K to T = 700 K, as listed in Table 11.

3.6. Thermodynamic functions for the condensed states. Derived molar entropies and molar enthalpies under vapor saturation pressure for the condensed phases of 3MP relative to that of the crystals at T0 K are listed in Table 11. Smoothed molar heat capacities were integrated, and the molar entropy and enthalpy of melting are added at T = Ttp = 335.608 K. Pre-melting corrections were made with published methods36 for solid-insoluble impurities and the mole-fraction purity x = 0.9997.

3.6. Enthalpy of combustion and derived enthalpy of formation for the crystalline state. Results of a typical combustion experiment for 3MP are listed in Table 12, where symbols and abbreviations follow reference .Measured values of cU°/Mfor all seven combustions are reported in Table 13, where these refer to the reaction:

C15H12(cr) + 18 O2(g) = 15 CO2(g) + 6 H2O(l).	(3)

The derived standard energy of combustion Δc, standard enthalpy of combustion Δc, and the standard enthalpy of formation Δf for the crystal phase are listed in Table 13. Values are based on the sample mass, as CO2 recoveries were quantitative. Values of Δc and Δc refer to reaction (3), and the value of Δf refers to the reaction:

15 C(cr, graphite) + 6 H2(g) = C15H12(cr).	(4)

Uncertainties given in Table 13 are expressed as the "uncertainty interval" defined in reference, which is equivalent to the expanded uncertainty with 0.95 level of confidence. The standard enthalpies of formation of CO2(g), and H2O(l) were those assigned by CODATA [(393.51 ± 0.13) kJ∙mol1 and (285.830 ± 0.042) kJ∙mol1, respectively].

3.7. Thermodynamic functions in the ideal-gas state derived from experiment. Thermodynamic properties in the ideal-gas state (p°= 101.325 kPa) for 3MP are listed in Table 14. Results given in Tables 9 and 11 were used in combination with the enthalpy of formation for the crystals at T = 298.15 K (Table 13). Enthalpies and entropies for N2(g), equilibrium hydrogen, and graphite were determined from the JANAF tables, as described in Part 1.1

3.8. Computation of entropies for the ideal-gas state. The molecular parameters computed in this work and used for generation of ideal-gas entropies are given in Table 15. The methyl torsion rotational constant was computed for the equilibrium geometry (B3LYP/def2-QZVPD) following reference . To the best of our knowledge, there are no literature data, either experimental or computational, that these results can be compared with. The only two computational DFT studies that considered 3MP, do not report any explicit molecular parameters of relevance to this work.

Table 15 also lists computed values of the three-fold methyl torsion barrier computed with several different methods. As seen, the results vary in the range of (1.4 to 1.7) kJ∙mol1. The best estimate obtained with LCCSD(T) extrapolated to the complete basis set (CBS) is 1.42 kJ∙mol-1. This approach was also used for 9MA,1 where the barrier was calculated to be 0.5 kJ∙mol-1. For the conditions of interest to the present study, the small barrier (less than 2 kJ∙mol-1) allows the use of simple free-rotor approximation without any meaningful loss of accuracy.1

Computed ideal-gas entropies for 3MP are listed in Table 16. As described in section 2.9, computations were done using two different models (free rotor and 2-D model) for contributions from the two lowest-frequency modes. The contributions from these modes (tor+vib) are listed explicitly in the table. Differences between the two models are small (~0.1R), but significant, as will be discussed in section 4.2.

3.8. Computation of the enthalpy of formation for the ideal-gas state. The enthalpy of formation of 3MP in the ideal-gas state was computed as described in section 2.10 and the resulting value for (g) is listed in Table 17. The value listed was adjusted to account for coupling for the lowest two vibrational frequencies.

4. Discussion

4.1. Comparisons with experimental property results in the literature. Numerous values of the normal melting temperature for 3MP have been reported in the literature as part of synthesis reports. These are typically within ± 3 K of our measured Ttp, which is in accord with the relatively large uncertainties expected for such studies. The single normal boiling range 623 < (T/K) <633 reported by Kruber et al. is consistent with our results within the broad uncertainty range given by the authors. No other physical property measurements for 3MP were found in the literature.

Entropies  for the ideal-gas state of 3MP and those of 9MA (from Part 11) are compared in Figure 2. The plotted differences are reduced by Rln(2) to account for the difference in internal rotation symmetry number  for 3MP ( = 3) and 9MA ( = 6). The symmetry-adjusted entropies for 3MP and 9MA are seen to be nearly identical over the entire temperature range (300 < (T/K) < 650). The expanded uncertainty (0.95 level of confidence) in the differences is estimated to be a constant 0.17R (dotted lines in the figure). The larger uncertainties shown in Figure 2 (solid curves) were computed under the assumption of an unconstrained extrapolation of the vapor pressures at low temperatures. As discussed later (section 4.3), the extrapolation is constrained. At high temperatures the dominant contribution to the uncertainty represented as solid curves arises from the uncertainties in the estimated virial coefficients for each compound. Errors here are likely to be systematic for the two closely related compounds, so this contribution is ignored in the uncertainty estimate for the entropy difference. The close agreement of these results lends support to application of a computational model for 3MP that is analogous to that used for 9MA.

4.2 Comparison of experimental and computed ideal-gas entropies. Entropies for the ideal-gas state of 3MP obtained through combination of experimental results (described in section 3.7), are given in Table 14 (column 4), while values derived with computational chemistry (described in section 3.8)  are given in Table 16.  was evaluated with two different models for the two lowest vibrational modes: free rotor (Table 16, column 3) and 2-D (Table 16, column 5). All remaining modes were accounted for with the harmonic oscillator approximation. The experimental and computed values of  are compared in Fig 3.

As seen in Fig. 3 (open circles), computations with the free-rotor model overpredict the experimental results beyond the evaluated, albeit tight, uncertainties. In Part 1,1 we reported a similar significant deviation of the free-rotor model from the experimental values for 9MA that was attributed to coupling of the two lowest frequency modes. Interestingly, in the case of 9MA the ideal-gas entropy was underpredicted with the free-rotor model, while for 3MP it is overpredicted. Considering the structural similarities between 9MA and 3MP and the fact that their experimental symmetry-corrected ideal-gas entropies are nearly identical (Figure 2), we postulated that the mode coupling seen for 9MA may also be present in 3MP. To test this premise, we substituted the contributions of the two lowest-frequency modes in 3MP with the semi-empirical 2-D coupling model of Nakagaki et al.13 developed for 9MA. The results of this exercise are also given in Table 16 (column 5) and in Fig. 3 (dashed curve). Application of the 2-D model yields excellent agreement (within ~0.1R) between the computed and experimental entropies for the entire temperature range (300 < T/K < 700).

Although the use of 2-D model for 9MA cannot be viewed as rigorous, it does appear to provide a correction necessary to achieve the agreement within the experimental uncertainties, thus suggesting the importance of low-frequency mode coupling for 3MP. A more rigorous study that includes a detailed ab initio mapping of the potential energy surface is beyond the scope of this work but would be beneficial in the future.

4.3 Constrained extrapolation of vapor pressures to low temperatures

In Part 1 (section 4.7), we showed that extrapolation of vapor pressures to low temperatures with the Wagner equation (eq 1) is sensitive to the exponent chosen for the final term. The exponent “4.5” was chosen in this research to yield differences between  and for the region of extrapolation (i.e., for T/K < 380), that were consistent with those evaluated within the region of the experimental vapor pressures (380 < (T/K) < 633). Adjustment of the final exponent insignificantly affects the results for temperatures within the experimental range and higher. This was well demonstrated in Part 1 for 9MA (section 4.7),1 and results for 3MP are analogous.

4.4 Comparison of experimental and computed ideal-gas enthalpies of formation. The enthalpy of sublimation Hm at T/K = 298.15 for 3MP was derived by summation of the enthalpy of vaporization of the liquid Hm (Table 9) and the enthalpy of melting Hm (derivable from values given in Table 11), both for the temperature T/K = 298.15. The value obtained is listed in Table 17. The enthalpy of formation in the ideal-gas state (g, 298.15 K) was derived by summation of the enthalpy of formation for the crystal  (Table 13) and the enthalpy of sublimation at T/K = 298.15. As seen in Table 17, agreement between the experimental and computed values for (g, 298.15 K) is excellent, with the values being within 1 kJmol1. Similar good agreement was seen previously for 9MA.1

5. Conclusions

In our work on a variety of aromatic ring systems, we have shown that modern methods of computational chemistry can be applied for evaluation of entropies1,12 and enthalpies of formation35 in the ideal-gas state with uncertainties near those of the best measurements available. The results of the present pair of articles (this work and Part 11) have highlighted a limitation in the computational approach in the case of coupled low-frequency vibrations. Future work will include extensions to partially saturated 2- and 3ring hydrocarbons, where additional challenges related to low-frequency out-of-plane vibrational modes may arise. Application of well-validated computational methods with quantified uncertainties in engineering software, such as the NIST ThermoData Engine (TDE) [-], can provide great improvement over widely used group-contribution and other correlation methods with uncertainties that are ill-defined or unknown.

ASSOCIATED CONTENT

Supporting Information. The route for the synthesis of 3-methylphenanthrene. These results are available free of charge at …

Acknowledgments

We gratefully acknowledge the contributions of Stephen E. Knipmeyer in the d.s.c. studies, An (Andy) Nguyen in the vapor-pressure measurements, Norris K. Smith in the combustion calorimetric measurements, I. Alex Hossenlopp and Aaron P. Rau in vapor transfer of chemical samples in preparation for the physical property measurements, and William V. Steele for helpful guidance to these experimentalists. The authors acknowledge the financial support of the Office of Fossil Energy of the U.S. Department of Energy (DOE). The experimental work was funded within the Processing and Downstream Operations section of the Advanced Oil Recovery (AOR) program. The property measurements were completed in Bartlesville, Oklahoma at the National Institute of Petroleum and Energy Research through BDM-Oklahoma under its contract with DOE for Management and Operations of the National Oil and Related Programs (NORP), Contract Number DE-AC22-94C91008. The article preparation and computations were carried out at the National Institute of Standards and Technology (NIST). Computations, in part, were performed on the NIST Baker-Jarvis HPC cluster. Products or companies are named solely for descriptive clarity and this neither constitutes nor implies endorsement by NIST or by the U.S. government.

References

Table 1. Sample Description and Summary of Experiments for 3Methylphenanthrene.

Property	Method	Temperature Range/K

heat capacity 	adiabatic calorimetry	6 to 520

triple-point temperature (cr, l, g)	adiabatic calorimetry

enthalpy of melting (cr to l)	adiabatic calorimetry

heat capacity	differential scanning calorimetry	355 to 715

density (l)	vibrating tube	373 to 523

vapor pressure	inclined-piston manometry	380 to 485

comparative ebulliometry	474 to 633

enthalpy of combustion	oxygen-bomb calorimetry	298.15

sample purity a	fractional melting

(mole fraction purity = 0.9997)

a	Purity was determined by fractional melting in an adiabatic calorimeter, as described in the text.

Table 2. Calorimeter and Sample Characteristics for the Adiabatic Calorimetric Measurements for 3Methylphenanthrene a

m/g	51.464

Vi(298.15 K) / cm3	61.78

Tcal/K	298.7

pcal/kPa	4.43

r(Tmax)	3.4

rmin	1.7

102.(dC/C)max	0.012

xpre	0.0003

a m is the sample mass corrected for buoyancy; Vi is the internal volume of the calorimeter vessel; Tcal is the temperature of the calorimeter when sealed; pcal is the pressure of the helium and sample when sealed; r(Tmax) is the ratio of the heat capacity of the full calorimeter to that of the empty at the highest temperature Tmax 523 K of these measurements; rmin is the minimum value of r observed in this study; (dC/C)max is the vaporization correction at the highest temperature measured (i.e., Tmax  523 K); and xpre is the mole-fraction impurity used for pre-melting corrections.

Table 3. Summary of the Fractional-Melting Study for 3-Methylphenanthrene a

F	T(F)/K

0.4115	335.566

0.6115	335.580

0.8115	335.586

Ttp = (335.608 ± 0.02) K b

x = 0.9997

a	F is the fraction melted at observed temperature T(F), Ttp is the triple-point temperature of pure compound, x is the derived mole-fraction purity of the sample.

b	Expanded uncertainty with 0.95 level of confidence.

Table 4. Measurements of Molar Enthalpy Increment totHm and Derived Results at Vapor-Saturation Pressure for 3Methylphenanthrene

Ti	Tf	Ttrs	DtotHm c	DtrsHm d

N a	h b

K	K	K	kJmol1	kJmol1

single-phase measurements in the crystal phase

15	1	128.486	222.148		13.453	0.006

15	1	222.140	272.689		10.067	0.002

15	1	272.667	328.963		13.618	0.012

18	1	89.582	188.751		11.597	0.000

18	1	188.751	282.420		17.788	0.004

18	1	282.330	328.183		11.249	0.006

19	1	247.441	289.567		9.092	-0.008

19	1	289.554	330.673		10.251	0.009

20	1	52.867	126.271		5.899	0.004

20	1	126.305	220.507		13.393	0.002

20	1	220.494	271.219		10.029	-0.008

20	1	271.197	329.495		14.084	0.015

21	1	100.562	204.466		13.173	0.004

21	1	204.447	274.890		13.587	-0.009

crystal-to-liquid phase transition

18	4	328.515	339.462	335.608	21.600	18.518

20	2	328.856	339.702		21.574	18.508

21	2	329.579	340.390		21.584	18.498

average	18.508

single-phase measurements in the liquid phase

24	1	341.769	427.015		28.544	-0.001

24	1	427.003	505.844		30.030	-0.004

a	Adiabatic series number.

b	Number of heating increments.

c	DtotHm is the molar energy input from the initial temperature Ti to the final temperature Tf. The relative expanded uncertainty for all values of DtotHm and DtrsHm for the crystal-to-liquid phase transition is 0.002 with 0.95 level of confidence. The uncertainty for Ttrs is given in Table 3.

d	DtrsHm is the net molar enthalpy of transition at the transition temperature Ttrs or the excess enthalpy for singlephase measurements relative to the heat-capacity curve described in the text and defined in table 11.

Table 5. Molar Heat Capacities Csat,m at Vapor-Saturation Pressure Measured with Adiabatic Calorimetry for 3Methylphenanthrene (R = 8.31446 JK-1mol-1) a

N b	<T>/K	DT/K	Csat,m/R c	N b	<T>/K	DT/K	Csat,m/R c

crystal

14	5.733	0.838	0.082	2	90.641	7.855	9.820

14	6.522	0.851	0.126	13	96.425	8.056	10.331

14	7.430	1.061	0.181	2	98.806	8.465	10.544

14	8.434	1.046	0.266	10	99.472	9.264	10.600

14	9.470	1.106	0.369	13	104.861	8.680	11.069

14	10.534	1.134	0.495	2	107.452	8.817	11.304

14	11.726	1.285	0.656	10	108.894	9.571	11.428

14	13.061	1.408	0.849	13	116.323	14.204	12.068

14	14.516	1.523	1.060	2	116.460	9.189	12.086

14	16.109	1.677	1.304	2	125.717	9.309	12.891

14	17.855	1.839	1.566	13	131.050	15.243	13.350

14	19.784	2.029	1.853	2	135.124	9.453	13.705

14	21.933	2.278	2.169	2	144.659	9.615	14.538

14	24.295	2.454	2.514	13	146.656	15.908	14.706

14	26.897	2.751	2.885	2	154.363	9.789	15.384

14	29.780	3.036	3.285	13	163.243	17.265	16.166

14	33.012	3.423	3.719	2	164.242	9.969	16.256

14	36.594	3.741	4.186	2	174.303	10.157	17.149

14	40.554	4.183	4.680	13	180.662	17.576	17.706

14	44.989	4.693	5.226	2	184.413	10.101	18.038

14	49.907	5.152	5.797	2	194.548	10.176	18.973

14	55.362	5.767	6.400	13	198.204	17.513	19.313

7	55.957	5.131	6.465	2	204.701	10.137	19.900

11	56.511	5.077	6.523	2	214.817	10.104	20.849

12	60.245	5.530	6.919	13	215.705	17.499	20.924

7	61.389	5.698	7.035	2	224.904	10.088	21.767

12	66.211	6.087	7.522	13	233.201	17.509	22.578

7	67.378	6.258	7.644	2	234.974	10.066	22.741

13	68.851	5.874	7.789	2	244.947	10.056	23.689

12	72.465	6.396	8.133	13	250.621	17.548	24.253

7	73.924	6.816	8.291	2	254.990	10.048	24.665

13	75.070	6.470	8.382	2	265.026	10.047	25.625

10	75.488	7.115	8.422	13	268.020	17.238	25.937

13	81.800	6.804	9.016	13	285.313	17.341	27.597

10	82.691	7.281	9.091	13	301.886	15.732	29.146

13	88.803	7.166	9.646	13	314.892	10.217	30.401

10	90.631	8.407	9.815	13	325.002	9.958	31.415

liquid

5	343.356	7.809	37.369	22	418.699	15.292	42.672

19	344.038	9.548	37.421	22	434.277	15.955	43.724

18	344.243	9.553	37.438	22	450.079	15.728	44.773

22	345.698	11.670	37.537	23	460.512	15.585	45.458

5	352.093	9.663	37.992	23	476.785	17.081	46.504

22	358.697	14.371	38.466	23	493.686	16.852	47.562

22	373.409	15.083	39.509	23	509.113	14.158	48.502

22	388.151	14.846	40.551	23	519.546	6.978	49.135

22	403.316	15.528	41.610

a	The relative expanded uncertainties (0.95 level of confidence) for the heat capacities are Ur(Csat,m) = (0.0140 – 0.0004(T/K)) for the temperature range {5 ≤ (T/K) ≤ 30}, and 0.002 for temperatures T ≥ 30 K. The expanded uncertainty for all temperatures U(T) is 0.01 K (0.95 level of confidence).

b	Adiabatic series number.

c Average heat capacity for a temperature increment of DT with a mean temperature <T>.

Table 6. Measured Vapor Pressures for 3-Methylphenanthrene.a

Method	T/K	p/kPa	p/kPa	U(p)/kPa	DT/K

IP	379.972	0.0231	0.0002	0.0004

IP	394.972	0.0557	0.0001	0.0004

IP	404.968	0.0962	0.0001	0.0004

IP	414.967	0.1609	0.0000	0.0004

IP	424.968	0.2619	0.0000	0.0004

IP	434.966	0.4148	-0.0001	0.0006

IP	444.965	0.6412	-0.0001	0.0006

IP	454.968	0.9690	0.0001	0.0006

IP	464.963	1.4323	-0.0003	0.0008

IP	474.965	2.0771	0.0000	0.0010

IP	479.959	2.4831	0.0001	0.0012

IP	484.963	2.956	0.000	0.001

Decane	473.924	2.000	0.000	0.001	0.098

Decane	481.987	2.666	0.000	0.001	0.088

Decane	493.944	4.000	0.001	0.001	0.061

Decane	502.878	5.333	0.000	0.001	0.038

Decane	516.153	7.999	0.000	0.002	0.024

Decane	526.106	10.666	0.001	0.002	0.019

Decane	534.155	13.332	0.000	0.002	0.011

Decane	542.512	16.665	-0.002	0.003	0.004

Decane	549.448	19.933	-0.002	0.003	0.003

Decane	558.569	25.023	0.000	0.004	0.002

Water	558.571	25.023	-0.001	0.005	0.002

Water	567.749	31.177	0.000	0.006	-0.001

Water	576.981	38.565	-0.001	0.007	-0.004

Water	586.260	47.375	0.003	0.009	-0.001

Water	595.599	57.817	-0.001	0.010	0.001

Water	604.984	70.120	0.003	0.012	0.001

Water	614.424	84.533	0.001	0.014	0.001

Water	623.910	101.33	0.00	0.02	0.001

Water	633.453	120.79	-0.01	0.02	0.02

a IP indicates results obtained with inclined-piston manometry. Water or decane refers to the material used as the standard in the reference ebulliometer; T is the condensation temperature of the sample; the pressure p for ebulliometric measurements was calculated from the condensation temperature of the reference substance; p is the difference between the experimental vapor pressure and that calculated with eq 1 and the parameters listed in Table 7; U(p) is the expanded uncertainty (0.95 level of confidence) calculated from eq’s 1 and 2 of Part 1.1 The expanded uncertainty for all temperatures U(T) is 0.004 K (0.95 level of confidence). T is the difference between the boiling and condensation temperatures (Tboil – Tcond) for the 3-methyl-phenanthrene sample.

Table 7. Parameters for the Wagner Vapor-Pressure Equation (eq 1), Riedel Density Equation (eq 2), Selected Critical Constants, and Derived Acentric Factor a

3-methylphenanthrene

A	-9.330758	Tc/K = (875 ± 20)

B	3.394031	pc/kPa = 2750

C	-4.253259	c/kg∙m-3 = 313.1

D	-2.850377	 = 0.5286

a	The critical temperature Tc was estimated with the method of Joback.38,39 The critical pressure pc and critical density c were estimated, as described in the text. The estimated values of pc and Tc are closely correlated. The expanded uncertainty (0.95 level of confidence) U(Tc) = 20 K corresponds to U(pc) ≈ 0.2pc. The relative expanded uncertainty (0.95 level of confidence) for c is Ur(c) ≈ 0.1.

Table 8. Measured Liquid Densities at Temperature T and Vapor-Saturation Pressure ρsat for 3-Methylphenanthrene. a

T/K	ρsat/(kgm-3)	100(ρsat- ρcs)/ρsatb	T/K	ρsat/(kgm-3)	100(ρsat- ρcs)/ρsata

373.12	1042.6	0.13	473.11	969.3	-0.04

398.12	1022.8	-0.11	498.11	951.5	0.07

423.11	1004.9	-0.13	523.11	932.0	0.07

448.11	986.9	-0.13

a The expanded uncertainties (0.95 level of confidence) are U(T) = 0.01 K and U(ρsat) = 0.002ρsat.

b Values of ρcs were calculated with the corresponding-states correlation given in the text (eq 2).

Table 9. Derived Enthalpies of Vaporization Hm for 3-Methylphenanthrene.a

T/K	Hm/(kJmol1)	T/K	Hm/(kJmol1)	T/K	Hm/(kJmol1)

298.15 b	80.03 ± 0.47	440.00	70.00 ± 0.27	600.00	59.09 ± 0.48

300.00 b	79.89 ± 0.45	460.00	68.66 ± 0.25	620.00	57.55 ± 0.60

320.00 b	78.44 ± 0.40	480.00	67.34 ± 0.23	640.00 b	55.93 ± 0.75

340.00 b	76.98 ± 0.37	500.00	66.03 ± 0.23	660.00 b	54.22 ± 0.91

360.00 b	75.55 ± 0.33	520.00	64.70 ± 0.25	680.00 b	52.41 ± 1.11

380.00	74.13 ± 0.32	540.00	63.35 ± 0.27	700.00 b	50.46 ± 1.33

400.00	72.73 ± 0.30	560.00	61.98 ± 0.32

420.00	71.36 ± 0.28	580.00	60.56 ± 0.38

a Uncertainties for Hm are expanded uncertainties with 0.95 level of confidence.

b The value at this temperature was calculated with extrapolated vapor pressures.

Table 10. Measured Two-Phase (liquid + vapor) Heat Capacities and derived Csat,m values for 3Methylphenanthrene (R = 8.31446 JK1mol1).a

T/K	/R	/R	/R	T/K	Csat,m/R

m/g	0.01011	0.01750	0.02345

Vcell/cm3	0.0531	0.0531	0.0560

355.0	38.21	38.16	38.12	360.0	38.39

375.0	39.48	39.50	39.50	380.0	39.90

395.0	40.89	40.95	40.74	400.0	41.36

415.0	42.49	42.39	42.34	420.0	42.76

435.0	43.63	43.74	43.80	440.0	44.12

455.0	44.64	44.97	44.88	460.0	45.44

475.0	45.99	46.37	46.40	480.0	46.71

495.0	47.20	47.76	47.69	500.0	47.94

515.0	48.30	48.80	48.77	520.0	49.14

535.0	50.75	50.52	50.13	540.0	50.31

555.0	51.99	51.38	51.59	560.0	51.46

575.0	53.56	52.57	52.35	580.0	52.58

595.0	55.34	53.91	53.68	600.0	53.68

615.0	56.02	55.24	54.91	620.0	54.77

635.0	57.49	56.31	55.89	640.0	55.85

655.0	58.41	57.51	56.56	660.0	56.93

675.0	60.77	58.72	58.51	680.0	58.01

695.0	62.92	60.15	59.72	700.0	59.11

715.0	65.13	61.39	61.50

a m is the mass of the sample corrected for buoyancy, Vcell is the internal volume of the d.s.c. cell at T = 298.15 K after sealing.

b The relative expanded uncertainty Ur for  and Csat,m is 0.02 with 0.95 level of confidence. The expanded uncertainty (0.95 level of confidence) for all temperatures U(T) is 0.2 K.

Table 11. Molar Thermodynamic Functions at Vapor-Saturation Pressure for 3Methylphenanthrene. (R = 8.31446 JK-1mol-1) a

T/K	Csat,m/R	/R	/RT	T/K	Csat,m/R	/R	/RT

crystal

5.00		0.056	0.019	0.014	160.00		15.879	15.929	8.391

10.00		0.429	0.147	0.110	180.00		17.649	17.901	9.321

20.00		1.885	0.879	0.626	200.00		19.475	19.855	10.245

30.00		3.314	1.918	1.287	220.00		21.328	21.798	11.168

40.00		4.612	3.052	1.959	240.00		23.227	23.735	12.093

50.00		5.808	4.212	2.611	260.00		25.163	25.670	13.024

60.00		6.892	5.369	3.236	280.00		27.090	27.606	13.960

70.00		7.901	6.507	3.831	298.15		28.798	29.360	14.811

80.00		8.847	7.624	4.399	300.00		28.972	29.539	14.898

90.00		9.754	8.719	4.944	320.00		30.908	31.470	15.838

100.00		10.645	9.793	5.470	330.00		31.950	32.437	16.310

120.00		12.389	11.888	6.478	335.608	b	32.564	32.980	16.576

140.00		14.127	13.929	7.446

liquid

298.15	b	34.189	35.414	21.664	500.00		47.949	56.421	29.562

300.00	b	34.320	35.625	21.741	520.00		49.160	58.325	30.293

320.00	b	35.730	37.885	22.572	540.00		50.317	60.202	31.013

335.608	b	36.824	39.613	23.209	560.00		51.460	62.053	31.723

340.00		37.132	40.094	23.387	580.00		52.582	63.878	32.423

360.00		38.559	42.256	24.190	600.00		53.684	65.679	33.113

380.00		39.977	44.379	24.984	620.00		54.771	67.457	33.794

400.00		41.381	46.466	25.769	640.00		55.853	69.213	34.467

420.00		42.761	48.518	26.545	660.00		56.929	70.949	35.131

440.00		44.108	50.538	27.313	680.00		58.012	72.664	35.788

460.00		45.425	52.528	28.072	700.00		59.114	74.362	36.439

480.00		46.708	54.489	28.822

a	Relative expanded uncertainties (0.95 level of confidence) Ur for all properties  for temperatures T/K < 520 are Ur() = (0.0140 – 0.0004(T/K)) for the temperature range (10 ≤ T/K ≤ 30), and 0.002 for temperatures T/K ≥ 30. The expanded uncertainty for the temperatures U(T) is 0.01 K for T/K ≤ 520 and 0.2 K for T/K > 520. For temperatures T/K > 520, Ur for the heat capacities increases approximately linearly from 0.002 to 0.02 at T/K = 700, while Ur for the integrated functions increases from 0.002 to 0.003.

b	Values at this temperature were evaluated through linear extrapolation of measured heat capacities for T/K < 460.

Table 12. Details of a Typical Combustion Experiment at T = 298.15 K (p° = 101.325 kPa) for 3Methylphenanthrene.a

m'(compound)/g	0.911152

m''(fuse)/g	0.001515

ni(H2O)/mol	0.05535

p(O2) / MPa	2.97

m(Pt)/g	20.810

T/K = (Tf – Ti + Tcorr)/K	2.18860

(calor)/(JK-1)	16641.6

(cont)(-T)/J	-40.8

Uign/J	0.75

U(corrected to standard states) b/J	22.2

-m'' (/M) (fuse)/J	25.7

(/M) (compound)/(J∙g-1)	-39964.7

a	m'(compound) and m''(fuse) are the masses of the studied compound and cotton fuse, respectively, adjusted to vacuum conditions; ni(H2O) is the amount of water added to the calorimetric bomb prior to the experiment; p(O2) is the initial pressure of oxygen in the bomb at room temperature (23.4 °C); m(Pt) is the mass of the platinum crucible; ΔT is the corrected temperature rise; Ti and Tf are the initial and final temperatures in the main period, and ΔTcorr is the heat-exchange correction; εcalor is the energy equivalent of the calorimeter; (cont)(T) = i(cont)(Ti - 298.15 K) + f(cont)(298.15 K - Tf  + Tcorr);  i(cont) and f(cont) are the energy equivalent of the contents of the bomb in the initial and final states, respectively; Uign is the energy to ignite the sample; U(corrected to standard states) is the energy correction to the standard state; /M is the specific combustion energy of a compound. Symbols and abbreviations in this table are in accord with those of reference 46.

b	Items 81 to 85, 87 to 90, 93, and 94 of the computational form of reference 46.

Table 13. Summary of Experimental Energy of Combustion Results and Molar Thermodynamic Functions for 3-Methylphenanthrene at T = 298.15 K and p° = 101.325 kPa

{(cU°/M)(3-Methylphenanthrene, cr)} / (J∙g-1)

-39969.9	-39964.7	-39969.4	-39968.3	-39967.1	-39975.5	-39966.4

<{(/M)(3-Methylphenanthrene, cr)} / (J.g-1)>	-39968.8 ± 4.3 b

(3-Methylphenanthrene, cr) / (kJ∙mol-1)	-7684.2 ± 0.8 b

(3-Methylphenanthrene, cr) / (kJ∙mol-1)	-7691.7 ± 0.8 b

(3-Methylphenanthrene, cr) / (kJ∙mol-1)	74.0 ± 2.1 c

a	Uncertainties for all molar values are the “uncertainty interval” as defined in reference 47. These values are equivalent to the combined expanded uncertainty with 95 percent level of confidence. The uncertainty listed for the specific energy of combustion is the standard deviation of the mean.

b	Value for the idealized combustion reaction:

C15H12(cr) + 18 O2(g) = 15 CO2(g) + 6 H2O(l).

c	Value for the formation reaction:

15 C(cr, graphite) + 6 H2(g) = C15H12(cr).

Table 14. Molar Thermodynamic Properties of the Ideal Gas State at p = p° = 101.325 kPa for 3Methylphenanthrene. (R = 8.31446 JK-1mol-1) a

T		b		c

K	RT	RT	R	R	RT	R	RT

298.15 d,e	53.95 ± 0.20	0.00	52.59 ± 0.20	0.00	68.99 ± 0.86	-51.99 ± 0.20	120.98 ± 0.86

300.00 d,e	53.77 ± 0.18	0.00	52.75 ± 0.20	0.00	68.49 ± 0.86	-52.06 ± 0.20	120.55 ± 0.84

320.00 d,e	52.05 ± 0.16	0.00	54.44 ± 0.16	0.00	63.55 ± 0.80	-52.75 ± 0.16	116.30 ± 0.80

340.00 d	50.62 ± 0.14	0.00	56.12 ± 0.16	0.00	59.19 ± 0.76	-53.39 ± 0.16	112.57 ± 0.74

360.00 d	49.43 ± 0.12	0.00	57.79 ± 0.14	0.00	55.33 ± 0.72	-53.97 ± 0.14	109.30 ± 0.70

380.00	48.45 ± 0.12	0.00	59.45 ± 0.14	0.00	51.90 ± 0.68	-54.51 ± 0.14	106.41 ± 0.68

400.00	47.64 ± 0.10	0.00	61.11 ± 0.12	0.00	48.82 ± 0.64	-55.00 ± 0.12	103.82 ± 0.64

420.00	46.98 ± 0.10	0.00	62.76 ± 0.12	0.00	46.07 ± 0.60	-55.44 ± 0.12	101.51 ± 0.60

440.00	46.45 ± 0.10	0.01	64.40 ± 0.12	0.00	43.58 ± 0.58	-55.84 ± 0.12	99.42 ± 0.58

460.00	46.03 ± 0.08	0.01	66.04 ± 0.12	0.01	41.33 ± 0.56	-56.21 ± 0.12	97.54 ± 0.56

480.00	45.71 ± 0.08	0.02	67.67 ± 0.12	0.01	39.28 ± 0.54	-56.54 ± 0.12	95.82 ± 0.54

500.00	45.47 ± 0.08	0.03	69.29 ± 0.12	0.02	37.41 ± 0.50	-56.84 ± 0.12	94.26 ± 0.52

520.00	45.29 ± 0.08	0.04	70.89 ± 0.12	0.03	35.71 ± 0.50	-57.12 ± 0.12	92.82 ± 0.50

540.00	45.18 ± 0.08	0.06	72.48 ± 0.14	0.04	34.14 ± 0.48	-57.37 ± 0.14	91.50 ± 0.48

560.00	45.11 ± 0.10	0.08	74.06 ± 0.14	0.06	32.69 ± 0.46	-57.60 ± 0.14	90.29 ± 0.48

580.00	45.09 ± 0.10	0.11	75.62 ± 0.16	0.08	31.36 ± 0.44	-57.81 ± 0.16	89.17 ± 0.46

600.00	45.10 ± 0.12	0.15	77.16 ± 0.16	0.11	30.12 ± 0.44	-58.00 ± 0.16	88.12 ± 0.44

620.00	45.15 ± 0.16	0.19	78.69 ± 0.20	0.14	28.98 ± 0.44	-58.18 ± 0.20	87.15 ± 0.44

640.00 d	45.22 ± 0.20	0.24	80.20 ± 0.22	0.18	27.91 ± 0.44	-58.33 ± 0.22	86.25 ± 0.46

660.00 d	45.32 ± 0.24	0.31	81.69 ± 0.26	0.23	26.92 ± 0.44	-58.48 ± 0.26	85.40 ± 0.46

680.00 d	45.44 ± 0.28	0.38	83.17 ± 0.30	0.29	26.00 ± 0.46	-58.61 ± 0.30	84.61 ± 0.48

700.00 d	45.58 ± 0.32	0.47	84.63 ± 0.36	0.35	25.14 ± 0.48	-58.72 ± 0.36	83.86 ± 0.50

a Uncertainties given in the table are expanded uncertainties at 0.95 level of confidence.

b Gas-imperfection correction that has been included in the listed molar enthalpy for the ideal gas. The molar enthalpy of the gas is calculated relative to that of the crystals at T0.

c Gas-imperfection correction that has been included in the listed molar entropy of the ideal gas.  =  + .

d Values at this temperat)ure were calculated with extrapolated vapor pressures calculated from the fitted parameters (Table 7) of the Wagner equation (eq 1).

e. Values at this temperature were calculated with extrapolated values of Csat,m for the liquid phase (Table 11).

Table 15. Computed Molecular Properties of 3-Methylphenanthrene.a

Rotational Constants (GHz)		Torsional Barrier (kJ∙mol-1)

A	1.278		B3LYP/def2-QZVPD	1.62

B	0.450		DF-MP2/aug-cc-pVQZ	1.71

C	0.333		LCCSD(T)/aug-cc-pVQZ	1.67

LCCSD(T)/aug-cc-pV5Z	1.55

LCCSD(T)/CBS	1.42

computed (unscaled) vibrational frequencies (cm-1)b

71.8c		78.8c	101.6	176.9	193.5	242.8	294.0	341.0	402.9

420.3	441.1	457.5	479.0	521.2	539.0	566.7	614.0	643.6

699.4	731.3	732.5	762.7	779.3	808.7	814.0	859.7	892.0

893.1	905.1	905.5	977.4	987.3	999.0	1009.2	1009.7	1056.9

1065.4	1066.5	1121.9	1175.1	1176.5	1189.3	1211.8	1223.3	1246.9

1268.3	1310.5	1323.1	1362.4	1377.1	1417.6	1435.3	1454.4	1460.8

1485.8	1490.3	1498.6	1546.0	1555.6	1602.1	1645.7	1656.2	1659.8

3021.5	3066.0	3101.3	3153.3	3156.3	3159.5	3169.0	3171.0	3175.1

3179.3	3186.1	3201.8

Computed methyl-torsion rotational constant (cm-1) d = 5.428

Symmetry number = 3

a Unless specified otherwise, the results were obtained at the B3LYP/def2-QZVPD level.

b Scaling factors used in entropy calculations were 0.9601 for hydrogen stretches and 0.9689 for all others, as noted in the text.

c For evaluation of ideal-gas thermodynamic properties, the two lowest-frequency modes were treated as (1) a one-dimensional free rotor (for the lower-frequency mode) and harmonic oscillator (“free-rotor” model), and (2) a coupled pair with the two-dimensional model of Nakagaki et al.13 (“2-D” model).

d Computed for equilibrium geometry computed with B3LYP/def2-QZVPD following reference 50.

TABLE 16. Computed Molar Thermodynamic Properties in the Ideal-gas State for 3-Methylphenanthrene at p = p° = 101.325 kPa (R = 8.31446 JK1mol-1).

Free-rotor Model a	2-D Model b

T/K	(tor+vib)/R b	/R c	(tor+vib)/R b	/R c	/RT d	/R e

298.15	3.80	52.81	3.70	52.71	0.000	24.72

300.00	3.81	52.97	3.71	52.87	0.153	24.89

320.00	3.90	54.63	3.81	54.53	1.753	26.63

340.00	3.99	56.29	3.90	56.20	3.267	28.35

360.00	4.08	57.96	3.99	57.86	4.707	30.02

380.00	4.16	59.62	4.07	59.53	6.083	31.65

400.00	4.24	61.29	4.15	61.19	7.401	33.24

420.00	4.31	62.95	4.22	62.85	8.668	34.76

440.00	4.38	64.60	4.29	64.50	9.887	36.23

460.00	4.45	66.24	4.36	66.15	11.06	37.64

480.00	4.51	67.87	4.42	67.78	12.20	38.99

500.00	4.57	69.48	4.48	69.40	13.30	40.29

520.00	4.63	71.09	4.54	71.00	14.36	41.53

540.00	4.69	72.68	4.60	72.59	15.39	42.72

560.00	4.74	74.25	4.65	74.16	16.38	43.85

580.00	4.79	75.81	4.70	75.72	17.35	44.94

600.00	4.84	77.35	4.76	77.26	18.29	45.98

620.00	4.89	78.88	4.80	78.79	19.20	46.98

640.00	4.94	80.38	4.85	80.29	20.08	47.93

660.00	4.99	81.87	4.90	81.78	20.94	48.85

680.00	5.03	83.34	4.94	83.25	21.77	49.72

700.00	5.07	84.79	4.99	84.71	22.58	50.57

a Contributions of the two lowest-frequency vibrational modes are represented with (1) a “free-rotor” model and (2) a model that accounts for coupling of the two modes; the “2-D” model.

b (tor+vib) is the contribution to the total entropy arising from the two lowest-frequency modes.

c  is the total entropy in the ideal-gas state that includes (torsion).

d  is the enthalpy of the ideal gas at temperature T relative to that at T = 298.15 K.

e Heat capacity of the ideal gas.

Table 17. Comparison of Computed and Experimental Ideal-gas Enthalpies of Formation (g) for 3Methylphenanthrene at Temperature T = 298.15 K.

Source	(cr)/(kJ∙mol-1)	Hm/(kJmol1)	(g)/(kJ∙mol-1)

This work (computed) a	172.1 ± 3.0

This work (experiment)	74.0 ± 2.1	97.0 ± 0.5 b	171.0 ± 2.2

a Computed with the method of Paulechka and Kazakov,35 as described in sections 2.10 and 3.8; decreased by 0.8 kJ∙mol-1 to account for mode coupling

b This value of the enthalpy of sublimation Hm(298.15 K)/(kJmol1) was derived from the experimental property of measurements of this research, as described in section 4.4.

.

Figure 1. Plot of molar heat capacities at saturation pressure Csat,m against temperature for 3-methyphenanthrene. The vertical line indicates the triple-point Ttp temperature. The smooth curve for temperatures T > 520 K represents results obtained with d.s.c. Heat capacities for the liquid for temperatures T < Ttp were estimated by linear extrapolation of measured values for temperatures T < 420 K.

Figure 2. Deviation plot between ideal-gas entropies derived from the experimental property measurements (expt) for 3methylphenanthrene (Table 14) and 9methylanthracene (Table 14 of Part 11). The dashed curve represents the symmetry-corrected differences. Solid curved lines represent the expanded uncertainty (0.95 level of confidence) for (expt) based on uncertainties given in the respective tables. Dashed lines represent the estimated expanded uncertainty (0.95 level of confidence). See section 4.1 of the text.

Figure 3. Deviation plot between ideal-gas entropies of 3-methylphenanthrene derived from the experimental property measurements (expt) (Table 14) and values computed with two different methods described in the text (computed) (Table 16). ○, (computed) was evaluated with free-rotor model; – – –, (computed) was evaluated with the 2-D model. Models are described in section 2.9 The solid curved lines represent the expanded uncertainty (0.95 level of confidence for (expt).

()	Kazakov, A. F.; Paulechka, E.; Chirico, R. D.  Reconciliation of Experimental and Computed Thermodynamic Properties for Methyl-Substituted 3-Ring Aromatics. Part 1: 9 Methylanthracene. J. Chem. Eng. Data, submitted.

()	Chirico, R. D.; Johnson, R.D. III; Steele, W.V.  Thermodynamic properties of methylquinolines: Experimental results for 2,6-dimethylquinoline and mutual validation between experiments and computational methods for methylquinolines. J. Chem. Thermodyn. 2007, 39, 698-711.

()	Chirico, R. D.; Steele, W.V.  Thermodynamic properties of tert-butylbenzene and 1,4-di-tert-butylbenzene. J. Chem. Thermodyn. 2009, 41, 392-401.

()	Chirico, R. D.; Kazakov, A. F.; Steele, W,V.  Thermodynamic properties of three-ring aza-aromatics. 1. Experimental results for phenazine and acridine, and mutual validation of experiments and computational methods. J. Chem. Thermodyn. 2010, 42, 571-580.

()	Chirico, R. D.; Kazakov, A. F.; Steele, W. V.  Thermodynamic properties of three-ring aza-aromatics. 2. Experimental results for 1,10-phenanthroline, phenanthridine, and 7,8-benzoquinoline, and mutual validation of experiments and computational methods. J. Chem. Thermodyn. 2010, 42, 581-590.

()	Chirico, R. D.; Kazakov, A. F.; Steele, W. V.  Thermodynamic properties of 9-fluorenone: Mutual validation of experimental and computational results. J. Chem. Thermodyn. 2012, 54, 278-287.

()	Chirico, R. D.; Steele, W. V.  Thermodynamic properties of 1-phenylnaphthalene and 2-phenylnaphthalene. J. Chem. Thermodyn. 2014, 73, 241-254.

()	Chirico, R. D.; Kazakov, A. F.  Thermodynamic properties of xanthone: Heat capacities, phase-transition properties, and thermodynamic-consistency analyses using computational results.  J. Chem. Thermodyn. 2015, 86, 90-95.

()	Chirico, R. D.; Steele, W. V.; Kazakov, A. F.  Thermodynamic properties of 1-naphthol: Mutual validation of experimental and computational results. J. Chem. Thermodyn. 2015, 86, 106-115.

()	Chirico, R. D.; Steele, W. V.; Kazakov, A. F.  Thermodynamic properties of indan: Experimental and computational results.  J. Chem. Thermodyn. 2016, 96, 41-51.

()	Chirico, R. D.; Kazakov, A. F.  Thermodynamic properties of pyrrole, 1-methylpyrrole, 2,4-dimethylpyrrole, and 2,5-dimethylpyrrole: Experimental and computational results. J. Chem. Thermodyn. 2018, 116, 213-229.

()	Chirico, R. D.; Paulechka, E.; Bazyleva, A.; Kazakov, A. F. Thermodynamic properties of 2-methylindole: Experimental and computational results for gas-phase entropy and enthalpy of formation. J. Chem. Thermodyn. 2018, 125, 257-270.

()	Nakagaki, M.; Nishi, E.; Sakota, K.; Nakano, H.; Sekiya, H.  A model two-dimensional potential for internal rotation of 9-methylanthracene studied by electronic spectroscopy and DFT calculations. Chem. Phys. 2006, 328, 190-196,

()	Steele, W. V.; Chirico, R. D.; Cowell, A. B.; Nguyen, A.; Knipmeyer, S. E.  Possible precursors and products of deep hydrodesulfurization of gasoline and distillate fuels. Part 2. The thermodynamic properties of 2,3-dihydrobenzo[b]thiophene. J. Chem. Thermodyn. 2003, 35, 1253-1276.

() 	Commission on Isotopic Abundances and Atomic Weights. Standard Atomic Weights. https://www.ciaaw.org/atomic-weights.htm (accessed June 14, 2021).

()	Tiesinga, E.; Mohr, P. J.; Newell, D. B.; Taylor, B. N. The 2018 CODATA Recommended Values of the Fundamental Physical Constants" (Web Version 8.1). Database developed by J. Baker, M. Douma, and S. Kotochigova. http://physics.nist.gov/constants, National Institute of Standards and Technology, Gaithersburg, MD 20899. (accessed June 14, 2021).

()	Steele, W. V.; Archer, D. G.; Chirico, R. D.; Collier, W. B.; Hossenlopp, I. A.; Nguyen, A.; Smith, N. K.; Gammon, B. E.  The thermodynamic properties of quinoline and isoquinoline. J. Chem. Thermodyn. 1988, 20, 1233–1264.

()	Swietoslawski, W.  Ebulliometric Measurements, Reinhold, New York, 1945.

()	Osborn, A. G.; Douslin, D. R. J. Chem. Eng. Data 1966, 11, 502-509.

()	Good, W. D.; Moore, R. T.  Enthalpies of formation of ethylenediamine, 1,2,-propanediamine, 1,2,-butanediamine, 2-methyl-1,2-propanediamine, and isobutylamine. C-N and N-F thermochemical bond energies. J. Chem. Eng. Data 1970, 15, 150-154.

()	Good, W. D.  Enthalpies of combustion of nine organic nitrogen compounds related to petroleum. J. Chem. Eng. Data 1972, 17, 28-31.

()	Good, W. D.; Scott, D. W.; Waddington, G.  Combustion calorimetry of organic fluorine compounds by a rotating-bomb method. J. Phys. Chem. 1956, 60, 1080-1089.

()	Good, W. D.; Douslin, D. R.; Scott, D. W.; George, A.; Lacina, J. L.; Dawson, J. P.; Waddington, G.  Thermochemistry and vapor pressure of aliphatic fluorocarbons. A comparison of the C-F and C-H thermochemical bond energies.  J. Phys. Chem. 1959, 63, 1133-1138.

()	van der Lee, A; Dumitrescu, D. G.  Thermal expansion properties of organic crystals: a CSD study. Chem. Sci. 2021, 12, 8537-8547.

()	Hubbard, W. N.; Scott, D. W.; Waddington, G. in F.D. Rossini (Ed.) Experimental Thermochemistry, Interscience, New York, 1956, pp. 75-128, Chapter 5. For those who cannot obtain a copy of this reference, the following source details the items in question, but in an earlier version in which some of the ancillary data are inaccurate. Hubbard, Ward N.; Scott, Donald W.; Waddington, G.  Reduction to Standard States (at 25°C) of Bomb Calorimetric Data for Compounds of Carbon, Hydrogen, Oxygen and Sulfur. J. Phys. Chem. 1954, 58, 152-162.

()	Paulechka, E.; Riccardi, D.; Bazyleva, A.; Ribeiro da Silva, M. D. M. C.; Zaitsau, D.  Corrections to standard state in combustion calorimetry: An update and a web-based tool. J. Chem. Themodyn. 2021, 158, 106425.

()	Good, W. D.; Smith, N. K.  Enthalpies of combustion of toluene, benzene, cyclohexane, cyclohexene, methylcyclopentane, 1-methylcyclopentene, and n-​hexane. J. Chem. Eng. Data 1969, 14, 102-106.

()	Chirico, R. D.; Kazakov, A.; Bazyleva, A.; Diky, V.; Kroenlein, K.; Emel′yanenko, V. N.; Verevkin, S. P.  Critical Evaluation of Thermodynamic Properties for Halobenzoic Acids Through Consistency Analyses for Results from Experiment and Computational Chemistry. J. Phys. Chem. Ref. Data 2017, 46, 023105.

()	Rappoport, D.; Furche, F.  Property-optimized Gaussian basis sets for molecular response calculations. J. Chem. Phys. 2010, 133, 134105.

()	Nagy, P. R.; Samu, G.; Kállay, M.  An integral-direct linear-scaling second-order Møller–Plesset approach. J. Chem. Theory Comput. 2016, 12, 4897-4914.

()	Nagy, P. R.; Samu, G.; Kállay, M.  Optimization of the linear-scaling local natural orbital CCSD (T) method: Improved algorithm and benchmark applications. J. Chem. Theory Comput. 2018, 14, 4193-4215.

()	Frisch, M. J.; Trucks, G. W.; Schlegel, H. B.; Scuseria, G. E.; Robb, M. A.; Cheeseman, J. R.; Scalmani, G.; Barone, V.; Petersson, G. A.; Nakatsuji, H. et al. Gaussian 16 Revision B.01. 2016; Gaussian Inc., Wallingford, CT.

()	Parrish, R. M.; Burns, L. A.; Smith, D. G. A.; Simmonett, A.C.; DePrince, A. E.; Hohenstein, E. G.; Bozkaya, U.; Sokolov, A. Yu.; Di Remigio, R.; Richard, R. M.; Gonthier, J. F.; James, A. M.; McAlexander, H. R.; Kumar, A.; Saitow, M.; Wang, X.; Pritchard, B. P.; Verma, P.; Schaefer, H. F.; Patkowski, K.; King, R. A.; Valeev, E. F.; Evangelista, F. A.; Turney, J. M.; Crawford, T. D.; Sherrill, C. D.  PSI4 1.1: An Open-Source Electronic Structure Program Emphasizing Automation, Advanced Libraries, and Interoperability. J. Chem. Theory Comput. 2017, 13, 3185-3197.

()	Smith, D. G. A.; Burns, L. A.; Simmonett, A.C.; Parrish, R. M.; Schieber, M. C.; Galvelis, R.; Kraus, P.; Kruse, H.; Di Remigio, R.; Alenaizan, A.; James, A. M.; Lehtola, S.; Misiewicz, J. P.; Scheurer, M.; Shaw, R. A.; Schriber, J. B.; Xie, Y.; Glick, Z. L.; Sirianni, D. A.; O’Brien, J. S.; Waldrop, J. M.; Kumar, A.; Hohenstein, E. G.; Pritchard, B. P.; Brooks, B. R.; Schaefer, H. F., III; Sokolov, A. Yu.; Patkowski, K.; DePrince, A. E., III; Bozkaya, U.; King, R. A.; Evangelista, F. A.; Turney, J. M.; Crawford, T. D.; Sherrill, C. D.  PSI4 1.4: Open-source software for high-throughput quantum chemistry. J. Chem. Phys. 2020, 152, 184108.

()	Kállay, M.; Nagy, P. R.; Mester, D.; Rolik, Z.; Samu, G.; Csontos, J.; Csóka, J.; Szabó, P. B.; Gyevi-Nagy, L.; Hégely, B.; Ladjánszki, I.  The MRCC program system: Accurate quantum chemistry from water to proteins. J. Chem. Phys. 2020, 152, 074107.

()	Paulechka, E.; Kazakov, A.  Efficient estimation of formation enthalpies for closed-shell organic compounds with local coupled-cluster methods. J. Chem. Theory Comput, 2018, 14, 5920-5932.

()	McCullough, J. P.; Waddington, G.  Melting-point purity determinations: limitations as evidenced by calorimetric studies in the melting region. Anal. Chim. Acta 1957, 17, 80-96.

()	Wagner, W.  New vapor pressure measurements for argon and nitrogen and a new method for establishing rational vapor pressure equations. Cryogenics 1973, 13, 470-482.

()	Poling, B. E.; O’Connell, J.; Prausnitz, J. M.  The Properties of Gases and Liquids, fifth ed., McGraw-Hill, New York, 2000.

()	Joback, K. G.; Reid, R. C. Estimation of pure-component properties from group contributions. Chem. Eng. Commun. 1987, 57, 233-243.

()	Riedel, L.  Liquid density in the saturated state. Extension of the theorem of corresponding states. II. Chem.-Ing.-Tech. 1954, 26, 259-264.

()	Hales, J. L.; Townsend, R.  Liquid densities from 293 to 490 K of nine aromatic hydrocarbons. J. Chem. Thermodyn. 1972, 4, 763-772.

()	Pitzer, K. S.; Curl, R. F., Jr.  Volumetric and thermodynamic properties of fluids. III. Empirical equation for the second virial coefficient. J. Am. Chem. Soc. 1957, 79, 2369-2370.

()	Orbey, H.; Vera, J. H.  Correlation for the third virial coefficient using Tc, Pc and ω as parameters AIChE J. 1983, 29, 107-113.

()	Steele, W. V.; Chirico, R. D.; Knipmeyer, S. E.; Smith, N. K.  Report NIPER-360, December 1988. Published by DOE Fossil Energy, Bartlesville Project Office. Available from NTIS Order No. DE89000709.

()	Steele, W. V.  Fifty years of thermodynamics research at Bartlesville: The Hugh M. Huffman legacy. J. Chem. Thermodyn. 1995, 27, 135-162.

()	Hubbard, W. N.; Scott, D. W.; Waddington, G. in: Rossini, F. D. (Ed.), Experimental Thermochemistry, Interscience, New York, 1956, pp. 75–128 (Chapter 5). For those who cannot obtain a copy of this reference, the following source details the items in question, but in an earlier version in which some of the ancillary data are inaccurate. Hubbard, W. N; Scott D. W.; Waddington, G.  Reduction to Standard States (at 25 C) of Bomb Calorimetric Data for Compounds of Carbon, Hydrogen, Oxygen and Sulfur. J. Phys. Chem. 1954, 58, 152–162.

()	Rossini, F. D.  Assignment of Uncertainities to Thermochemical Data. In: Rossini, F.D. (Ed.) Experimental Thermochemistry, Interscience, New York, 1956, pp. 297-320, Chapter 14.

()	Cox, J. D.; Wagman, D. D.; Medvedev, V. A.; Eds; CODATA Key Values for Thermodynamics. Hemisphere: New York, 1989.

()	Chase, M.W., Jr.; NIST-JANAF Thermochemical Tables. Fourth edition, Monograph 9 (Parts 1 and 2), J. Phys. Chem. Ref. Data, 1998, p. 1963.

()	Pitzer, K.S.,  Energy levels and thermodynamic functions for molecules with internal rotation: II. Unsymmetrical tops attached to a rigid frame. J. Chem. Phys. 1946, 14, 239-243.

()	Szczerba, M.; Rospondek, M.  Controls on distributions of methylphenanthrenes in sedimentary rock extracts: Critical evaluation of existing geochemical data from molecular modelling. Org. Geochem. 2010, 41, 1297-1311.

()	Hemelsoet, K.; Van Speybroeck, V.; Waroquier, M.  Bond Dissociation Enthalpies of Large Aromatic Carbon-Centered Radicals. J. Phys. Chem. A, 2008, 112, 13566-13573.

()	Kruber, O.; Marx, A.; Schade, W. The anthracene oil of coal tar. Ber. Dtsch. Chem. Ges. B 1938, 71B, 2478-2484.

()	Frenkel M.; Chirico R. D; Diky V.; Yan X.; Dong Q.; Muzny C.  ThermoData Engine (TDE): Software Implementation of the Dynamic Data Evaluation Concept. J. Chem. Inf. Model. 2005, 45, 816-838.

()	Diky, V.; Chirico, R. D.; Kazakov, A. F.; Muzny, C. D.; Frenkel, M.  ThermoData Engine (TDE): Software Implementation of the Dynamic Data Evaluation Concept. 3. Binary Mixtures. J. Chem. Inf. Model. 2009, 49, 503-517.

()	Diky, V.; Chirico, R. D.; Kazakov, A. F.; Muzny, C. D.; Frenkel, M.  ThermoData engine (TDE): software implementation of the dynamic data evaluation concept. 4. Chemical reactions. J. Chem. Inf., 2883 Model. 2009, 49-2896.

()	Diky, V.; Chirico, R. D.; Muzny, C. D.; Kazakov, A. F.; Kroenlein, K.; Magee, J. W.; Abdulagatov, I.; Kang, J. W.; Frenkel, M.  ThermoData Engine (TDE) Software Implementation of the Dynamic Data Evaluation Concept. 7. Ternary Mixtures. J. Chem. Inf. Model. 2012, 52, 260-276.

()	Diky, V.; Chirico, R. D.; Muzny, C. D.; Kazakov, A. F.; Kroenlein, K.; Magee, J. W.; Abdulagatov, I.; Frenkel, M.  ThermoData Engine (TDE): Software Implementation of the Dynamic Data Evaluation Concept. 9. Extensible Thermodynamic Constraints for Pure Compounds and New Model Developments.  J. Chem. Inf. Model. 2013, 53, 3418-3430.

()	Diky, V.; Chirico, R. D.; Frenkel, M.; Bazyleva, A.; Magee, J. W.; Paulechka, E.; Kazakov, A. F.; Lemmon, E. W.; Muzny, C. D.; Smolyanitsky, A. Y.; Townsend, S.; Kroenlein, K.  NIST ThermoData Engine, NIST Standard Reference Database 103b-Pure Compounds, Binary Mixtures, Ternary Mixtures, and Chemical Reactions, version 10.4.2; Standard Reference Data Program, National Institute of Standards and Technology: Gaithersburg, MD, 2021.