REVISION 1:

Coordinated Neutron and X-ray Computed Tomography of Meteorites: Detection and Distribution of Hydrogen-Bearing Materials

Allan H. Treiman

Lunar and Planetary Institute

Universities Space Research Association

3600 Bay Area Boulevard

Houston TX 77058

treiman@lpi.usra.edu

Jacob M. LaManna

Physical Measurement Laboratory

National Institute of Standards and Technology

Gaithersburg, Maryland 20899

Daniel S. Hussey

Physical Measurement Laboratory

National Institute of Standards and Technology

Gaithersburg, Maryland 20899

Isabella DeClue

University of Chicago

Chicago Illinois 60637

Lawrence M. Anovitz

Chemical Sciences Division

Oak Ridge National Laboratory

Oak Ridge, Tennessee, USA 37830

# Abstract

The presence and distribution of hydrogen-bearing materials in meteorites are important constraints on processes in the early solar system, and the delivery of volatile constituents to growing planets. Here, we show that coordinated neutron- and X-ray computed tomography, NXCT, can reveal the presence and distributions of hydrogen-bearing materials in meteorites, and thus help constrain presence and actions of water in the early solar system. NXCT is nearly non-destructive of meteorite samples. Neutron fluence in NXCT is approximately seven orders of magnitude less than in typical instrumental neutron activation analysis (INAA), and so produces little residual radioactivity and currently undetectable changes in isotope ratios. Heating during NXCT is minimal, but NXCT will overprint the record of cosmic ray exposure held in natural thermoluminescence.

Two meteorites were examined. EET 87503 is a howardite, a regolith breccia inferred to be from the asteroid 4 Vesta, and contains fragments of eucrite basalt, diogenite pyroxenite, and H-rich carbonaceous chondrites. With NXCT, the chondrite fragments within the meteorite piece can be clearly located and characterized, in preparation for possible extraction and detailed analyses. GRA 06100 is a CR2 chondrite meteorite that contains abundant iron metal and H-bearing silicates from aqueous alteration. In NXCT, H-bearing altered material is clearly distinguished from metal, and its distribution in three dimensions is revealed as a constraint on the processes of alteration.

# Introduction

Geological materials are physically and chemically heterogeneous, for examples bubbles in glass, different minerals, chemical zoning in minerals or glasses, etc. The three-dimensional characteristics of this heterogeneity have commonly been characterized by generalization from two-dimensional slices, i.e., the field of stereology (Russ, 1986). Practical examples of geological stereology include analyses of crystal size distributions, CSD (Cashman and Ferry, 1988), and interpretations of chondrule sizes (Eisenhour, 1996). With the advent of tomographic techniques, reconstruction of 3-D density distributions via penetrating radiation, it has become possible to directly access and image the heterogeneous internal structures of geological materials in 3D (Carlson, 2006; Mees et al., 2003). The most common tomographic technique is X-ray computed tomography (XRCT or XCT), in which the degree of X-ray attenuation (absorption and scattering) is mapped; the strength of X-ray attenuation is a monotonic function of atomic number, Figure 1 (Ebel and Rivers, 2007), as X-rays are scattered principally by electrons.

Figure 1. Relative attenuation cross-sections of X-rays and thermal neutrons by major elements, shown as effective ‘target’ areas. X-ray cross-sections increase monotonically with atomic number. Hydrogen and Cl have highest neutron cross-sections among the most abundant elements in the Earth’s crust; some trace elements have much higher cross-sections; e.g., the neutron cross-section for Gd would be a circle of 25 times the diameter of that for H. Cross-sections shown at different scales -- the X-ray attenuation cross-section of Fe for 90-KeV X-rays, interpolated from data in Hubbell and Seltzer (1996), is 45 barns (10-24 cm2); the total attenuation cross-section of thermal neutrons in Fe is ~14 barns (Sears, 1992).

X-ray computed tomography (XCT) has found significant use in studies of planetary materials, following the first reported application by Arnold et al. (1983). Ebel and Rivers (2007) and Hanna and Ketcham (2017) have reviewed applications of XCT to planetary materials, most of which have been chondrite meteorites. XCT work on chondrites has included studies of: general textures and fabrics (Duchnik et al., 2012; Ebel et al., 2008; Hezel et al., 2013; Matsumoto et al., 2013; Tait et al., 2014), chondrule sizes (Charles et al., 2018; Friedrich, 2008; Robin and Charles, 2015), sizes and shapes of metal grains (Friedrich et al., 2014; Ruzicka et al., 2015), organic matter (Matsumoto et al., 2013), porosity (Friedrich and Rivers, 2013; Sasso et al., 2009), aqueous alteration (Hanna et al., 2015), and deformation textures (Krzesińska, 2011).

Achondrite meteorites have seen less XCT study, most of which has been on lunar and martian samples. Studies of martian meteorites have emphasized the distribution of alteration materials (‘iddingsite’) in the nakhlites (Needham et al., 2013; Tomkinson et al., 2015). A few studies have looked at mineral and melt abundances and distributions in shergottites (do Nascimento-Dias et al., 2018; Ebel and Rivers, 2007; Gnos et al., 2002; Uesugi et al., 2010). Studies involving lunar samples have emphasized identification and characterization of fragments in breccias (Treiman and Coleff, 2018; Treiman and Semprich, 2019; Zeigler, 2014; Zeigler et al., 2017), and exploration of core samples from the Apollo missions (Jolliff et al., 2021; Zeigler et al., 2020). other studies have used XCT to locate specific crystals in lunar glass spherules (Ebel et al., 2005), and to characterize the 3D shapes of lunar regolith particles (Chiaramonti et al., 2017). XCT studies of other achondrites are few, seemingly limited to evaluation of porosity (Riad et al., 2014), and general investigations of the Almahatta Sitta polymict ureilite (Shaddad et al., 2010; Zolensky et al., 2010).

Neutron computed tomography (NCT) is another important probe of geological materials, in which total attenuation of neutrons (absorption and scattering) can be mapped in three dimensions (Hess et al., 2011; LaManna et al., 2017; Winkler, 2006). Thermal (cold) neutrons are attenuated strongly by hydrogen and chlorine (Fig. 1), making the technique ideal for study of aqueous processes and products in geological materials. NCT of geological materials has, in fact, emphasized the distributions of water and of hydrogen-bearing phases, e.g., Perfect et al. (2014), Anovitz et al. (2016), and Kaloyan et al. (2017).

There have been significantly fewer studies of geological materials by NCT than by XCT, at least in part because of the relative rarity of neutron sources and tomography laboratories. The techniques are complementary in that X-ray and neutron attenuations show different sensitivities to elements (and isotopes), see Figure 1. Canella et al. (2009) and Hess et al. (2011) gave the first planetary-related examples: a NCT image of a fragment of the Allende chondrite, and NCT and XCT of a tektite. Duchnik et al. (2012) demonstrated NCT and XCT on a fragment of the Allende meteorite. Jenniskens et al. (2012) used XCT and NCT data to explore the interior structure of fragments of the Sutter’s Mill chondrite. Pakhnevich (2016) used NCT’s sensitivity to H to search for water and organic matter in chondrite meteorites, and Treiman et al. (2018) is the precursor to this work. Kichanov et al. (2019) presented several NCT slices through a sample of the newly-fallen Chelyabinsk meteorite (LL5), and used them to locate particles of metal and their chemical interaction (Fe-diffusion) with surrounding silicates. Needham et al. (2020) presented coordinated neutron and X-ray tomographs of fragments of the Murchison (CM2) and Parnallee (LL3) chondrites, and Martell et al. (2021) showed that coordinated neutron and X-ray tomography could be used to locate meteorite fragments in impact ejecta.

Iron meteorites have also attracted interest, particularly because of neutron tomography’s capability to distinguish between Ni-rich and Ni-poor metals, i.e. taenite and kamacite, see Figure 1 (Caporali et al., 2016; Peetermans et al., 2013). Neutron diffraction has also been used to determine residual stresses in meteoritic iron (Caporali et al., 2018), and the spatial distributions of metal and silicates in a stony iron meteorite (Kichanov et al., 2018).

## Meteorite Targets

Here, we target meteorite samples that exemplify two of the most likely uses for coordinated NCT and XCT: the howardite EET 87503 as a meteoritic breccias; and the CR2 chondrite GRA 06100 as an example of aqueous alterations.

Most meteorites are fragmental at some level – chondrites are composed of individual chondrules and rock fragments (Briani et al., 2012; Greshake et al., 2002; Rubin and Bottke, 2009), and many achondrite are breccias of related or unrelated fragments. The most common achondrites, the HED meteorites (howardites, eucrites, diogenites), are inferred to be from the asteroid 4 Vesta; they are composed of fragments of its indigenous igneous rocks with some foreign components (Cartwright et al., 2014; Mittlefehldt, 2015; Mittlefehldt et al., 2013; Righter and Garber, 2011). Many HEDs, especially the howardites, contain fragments of carbonaceous chondrites, hydrogen-bearing material from outside the HED parent body (Herrin et al., 2010). These carbonaceous hydrous materials, which provide critical information about mixing early in the evolution of the asteroid belt, should be easily detectable by NCT because of their H contents. Similar fragments are present in some ordinary chondrites (Briani et al., 2012; Greshake et al., 2002; Krzesińska and Fritz, 2014; Rubin and Bottke, 2009), and in polymict ureilite meteorites (Beard et al., 2015; Brearley, 1992; Goodrich et al., 2004; Shaddad et al., 2010). The latter are particularly important, as the ureilites appear to have formed in a region of the early solar system distant from the formation area of carbonaceous meteorites (Warren, 2011).

Lunar samples present a different opportunity for NCT and XCT. Lunar regolith, returned samples or meteorites, contains fragments of asteroidal or cometary materials that impacted the moon, and so contain a record of bombardment in the Earth-Moon system (Joy et al., 2012; Zolensky, 1997). Similarly, lunar regolith can contain fragments of rare and significant lithologies, which would be difficult or impossible to locate and characterize without XCT or NCT (Gross et al., 2020; Treiman and Semprich, 2019; Zeigler, 2014; Zeigler et al., 2017; Zeigler et al., 2020). Most recently, XCT has been being used to guide the dissection of an Apollo 11 core tube sample, and pinpoint the larger fragments therein for special care (Jolliff et al., 2021; Zeigler et al., 2020).

Many meteorite samples, originally anhydrous, have been subjected to aqueous alteration, which has left water-bearing minerals in its wake. As noted above, the martian nakhlite meteorites contain veinlets and patches of clay minerals and hydrous iron oxides, which formed during aqueous alteration on Mars (Hicks et al., 2014; Lee et al., 2015; Needham et al., 2013; Tomkinson et al., 2015; Treiman et al., 1993). Similarly, many carbonaceous chondrites were affected by aqueous alteration on their asteroidal parent bodies (Abreu and Singletary, 2011; Abreu and Stanek, 2009; Harju et al., 2014). NCT, being sensitive to both hydrogen and chlorine, is an ideal method for locating and characterizing the distributions of these alterations.

# Samples and Methods

## Samples

### EET 87503

EET 87503 is a howardite meteorite of 1734.5 grams, a regolith breccia from the Eucrite Parent Body, which is generally inferred to be the asteroid 4 Vesta (Cartwright et al., 2014; Mittlefehldt, 2015; Mittlefehldt et al., 2013; Righter and Garber, 2011). It was found on the Elephant Moraine in Antarctica in 1987, and is paired with EET 87513 which was discovered nearby (Mittlefehldt et al., 2013; Righter and Garber, 2011). EET 87503 is typical of howardites, being a breccia composed primarily of fragments of diogenite orthopyroxenite and eucrite basalt. EET 87503 is unusual in containing few fragments of impact breccias, and in containing moderately abundant clasts of carbonaceous chondrite material (Buchanan and Mittlefehldt, 2003; Buchanan et al., 1993). EET 87503 is also rich in solar noble gases (Cartwright et al., 2014), which indicates that it (or its progenitor materials) sat at the surface of Vesta for significant time.

Figure 2. The studied samples. a) Howardite EET 87503,73. Black fusion crust at top surface, note white fragments of diogenite pyroxene, and small black fragments of carbonaceous chondrite material. b) CR2 chondrite GRA06100,84. Light-colored rounded chondrules in a fine-grained black matrix.

Most of the carbonaceous chondrite clasts in howardites, including those in EET 87503, are similar to CM2 chondrites like Murchison (Buchanan and Mittlefehldt, 2003; Zolensky et al., 1996), and have been heated to varying degrees. These CM2 fragments contain water-bearing minerals, notably serpentine and serpentine-like phyllosilicates (Zolensky et al., 1996). Other howardites contain clasts of CR2-like material, comparable to the Renazzo chondrite and GRA 06100 described below (Zolensky et al., 1996); none has been reported in EET 87503 (Buchanan and Mittlefehldt, 2003; Buchanan et al., 1993).

For this study, the Meteorite Working Group (MWG) and the Antarctic Meteorite Curator (ARES/JCS) loaned the fragment EET 87305,73 (Figure 2a). It weighs 11.098 grams and appears typical of the whole meteorite. It was returned to Meteorite Curation after tomography.

### GRA 06100

GRA 06100 is a CR2 chondrite, with a total mass of 421.75 grams (Abreu and Bullock, 2013). As a group, CR2 chondrites are rich in Fe-Ni metal, have relatively large chondrules, and show significant alteration of anhydrous silicate minerals to phyllosilicates (serpentines, clays), hydroxides, and amorphous materials that contain H as hydroxyl and/or bound water (Weisberg et al., 2006; Weisberg et al., 1993). There has been little work specifically on GRA 06100, but it has been included in many latitudinal studies of CRs, including those emphasizing: oxygen isotopes (Schrader et al., 2011); oxidation states (Schrader et al., 2013); organic matter (Cooper and Rios, 2016); metal compositions (Briani et al., 2013); water abundance and metamorphism (Garenne et al., 2016); phyllosilicate mineralogy (Howard et al., 2015); and presolar grains (Leitner et al., 2011).

GRA 06100 is of particular interest because it had been dehydrated and then partially rehydrated. GRA 06100 experienced an early heating event, as evidenced by its nearly anhydrous matrix (Briani et al., 2013; Garenne et al., 2016), textural equilibration in the matrix (Garenne et al., 2016), and lower abundances of C and N than most other CR chondrites (Humayun et al., 2013). Some thin sections of GRA 06100 show evidence of low-temperature water-bearing minerals that appear to post-date this metamorphism (Abreu and Bullock, 2013; Abreu and Singletary, 2011; Abreu and Stanek, 2009), but other sections do not contain water-bearing minerals (Harju et al., 2014). Thus, the distribution of water-bearing minerals may be strongly heterogeneous and of interest for understanding aqueous alteration processes in the CR parent asteroid.

For this study, the MWG and the Antarctic Meteorite Curator loaned an 8.691 gram fragment GRA 06100,84 (Figure 2b). It appears typical of the meteorite as a whole; the fragment was returned to Meteorite Curation after tomography.

## Methods

### The NIST-NeXT System

The NeXT system provides coordinated neutron and X-ray tomography by simultaneously imaging a sample with beams of thermal (slow) neutrons and X-rays at right angles to each other (LaManna et al., 2020a; LaManna et al., 2020b; LaManna et al., 2017). The NIST-NeXT system is described in detail in LaManna et al. (2017) and LaManna et al. (2020b), and crucial details are repeated here. The NeXT system is on the BT-2 beamline at the NIST Center for Neutron Research (NCNR); Figure 1 of LaManna et al. (2020b) shows its physical layout. The beamline produces thermal neutrons at fluence rates between 3x107 to 8x105 cm-2 s-1 with a beam diameter of 26 cm. The beam is concentrated and collimated, and then apertured to ~ 1 cm before impinging on the target. X-rays from a point source impinge on the sample at right angles to the neutron beam. The bremsstrahlung X-ray beam is polychromatic, with a maximum energy of 90 keV, and a mean energy of 44.33 keV with 2 mm of aluminum filtration. Neutrons and X-rays are detected by different P43 scintillator screens (gadolinium oxysulfide doped with terbium, Gd2O2S:Tb, also known as GadOx), which are imaged with Andor NEO scientific complementary metal oxide semiconductor (sCMOS) cameras. The cameras have 2560 by 2160 square pixels, each being 6.5 μm across, and can provide a neutron image resolution of ~20 μm (limited by the light bloom from the GadOx scintillator screen). To achieve higher spatial resolution, NCNR has developed an infinity corrected macroscope that allows neutron imaging at spatial resolutions less than 10 μm (Hussey et al., 2017; LaManna et al., 2020b). The NCT tomograms reported here, however, have a reconstructed voxel dimension of 15 µm with a minimum resolution of 30 µm.

Additional data are provided in SOM-1, and the raw image slices for neutron and X-ray tomograms are available in SOM-2.

### Data Processing

Following computed tomography reconstructions on the XCT and NCT data, the two tomograms were registered using a MATLAB (2021) routine developed at NIST, based on the Matlab multi-modal image registration function “imregister”. The rigid-body registration procedure accounts for: differences in voxel size; the approximately 90° difference between the X-ray and neutron beams and detectors; small differences in pitch and roll; and offsets in the three spatial directions. Because the two CT volumes have different sources of image contrast, the preferred metric for determining the best rigid body registration is maximization of the Mattes mutual information statistic (Mattes et al., 2001) rather than the datasets’ intensity cross-correlation. The tomograms are first registered coarsely, using versions of the tomograms down-sampled by a factor of 5 – 10 (volume reduction of 53 to 103). Down-sampling reduces noise and allows computation times on the order of minutes. The coarse registration is then refined on the full dataset to determine the affine translation parameters and apply them to properly register the tomograms (LaManna et al., 2020b)

### Phase Segmentation and Visualization

Phase segmentation, i.e., identifying and tagging specific materials and groups of materials by their attenuations of X-rays and neutrons, was done using Dragonfly© (DRAGONFLY, 2021). Each pair of registered tomogram image stacks (X-ray and neutron) was uploaded to Dragonfly and examined for structure and consistency. Identification of particular materials or groups of materials was via bivariate histograms, in which the attenuations (i.e., contrast) for X-rays and neutrons of each image voxel are plotted as a point. Dragonfly allows points or groups of points to be selected and tagged (e.g., by color) in this ‘histogram space,’ and simultaneously selected and tagged in ‘image space’ and displayed in two or three dimensions. In this manner, the locations of selected materials in the meteorite samples can be visualized (LaManna et al., 2020a), see Figures 3, 6, S1, and S4 . The bivariate histograms for EET 87503 and GRA 06100 are discussed below.

# Results

Our study demonstrates some of the utilities and advantages of coordinated neutron and X-ray tomography in the study of meteorites. In brecciated planetary samples, like EET 87503, it permits the identification and location of unusual fragments, both exogenous and indigenous in the sample. For instance, clasts of carbonaceous chondrite material deep within a meteorite fragment (not exposed at cut or broken surfaces) can be located and characterized to some extent. For other planetary samples, coordinated tomography can permit location of minerals and structures rich in volatile components, i.e., hydrogen and chlorine (Fig. 1). The distributions of water and chlorine in

Figure 3. EET 87503,73. (a) Bivariate histograms of neutron attenuation (x-axis) versus X-ray attenuation (y axis) for the registered tomograms. Color scale on right indicates number of voxels with given neutron- and X-ray attenuations (‘Sand’ palette in Dragonfly) – white circumscribed regions (labelled 1 & 3) have the greatest number of voxels. Negative values of attenuations are not physical, and represent both Poisson counting statistics and effects of flat-fielding. Labelled regions represent: 1, void space, plagioclase feldspar, Al metal packing/support; 2, plastic mounting substrate; 3, anhydrous Mg-rich silicates (diogenitic pyroxene); 4, anhydrous Fe-rich silicates (eucritic pyroxene); 5, hydrous magnesian minerals; 6, Fe-Ti-Cr oxides; and 7, Fe-rich metal and sulfide. See Supplemental Material for presentations in other color palettes.

a planetary sample can constrain the alteration processes that introduced these elements, and locate subsamples for additional analyses.

### Planetary Breccia: EET 87503

EET 87503, a howardite (Fig. 2a), exemplifies the value of coordinated NXCT for breccia samples like most meteorites and lunar materials. As with other howardite meteorites, EET 87503 is a breccia containing a wide range of materials: magnesian to ferroan orthopyroxenes derived from diogenites, basaltic fragments of many textures, impact melts, and carbonaceous chondrite (CC). Most CC contain hydroxyl-bearing minerals and have been used to help understand the distribution and isotopic compositions of hydrogen (i.e., water) in the early solar nebula. NXCT is ideally suited to locate CC clasts in howardites, and thus allow their extraction for coordinated chemical and isotopic analyses.

Figure 4. EET 87503,73 - a planar slice of the X-ray tomogram (in gray), with phases segmented according to the bivariate histogram of Figure 3 (contrast enhanced). Scale bar is 1 cm. Hydrous carbonaceous chondrite material (region 5) in green; Fe-rich eucritic pyroxene (region 4) in purple; Fe-Ti-Cr oxides (region 6) in orange. See Supplemental Materials for segmentation definitions on the bivariate attenuation histogram.

The bivariate histogram for EET 87503,73 shows a clear separation of materials according to their attenuations, Figure 3 (see SOM1 for details of the histographic regions). In that Figure, area #1 (minimal attenuation of both X-rays and neutrons) represents open space around the sample and anhydrous packing material (like aluminum). The small amount of plastic supporting the sample appears as area #2 -- low X-ray attenuation (~0.2) due to the low average atomic number and density and moderate neutron attenuation (to 2.5) due to the hydrogen in the plastic. Most of the meteorite plots as area #3, which is inferred to represent diogenitic, magnesian pyroxene (Mittlefehldt et al., 2013; Righter and Garber, 2011). The meteorite contains a small proportion of basaltic, eucritic material, with more ferroan pyroxene, which is identified as the region #4. EET 87503 contains small proportions of pyrrhotite (FeS), ilmenite (FeTiO3), and chromite spinel (ideally FeCr2O4), which appear in Figure 3 as region #6 – the iron in these minerals contributes to its neutron attenuation (Fig. 1), while the Ti and Cr contribute to X-ray attenuation without significant neutron attenuation. Finally, the meteorite contains scattered small grains of Fe-rich metal, and pixels containing them (and other phases) spread up to area #7, with high X-ray attenuation and intermediate neutron attenuation. The distinct peak at #5, with moderate X-ray attenuation and very high neutron attenuation, is correlated to hydrous ferroan silicates like serpentines and smectites. In EET 87503, this latter material occurs only in fragments of CM-like carbonaceous chondrites, (Buchanan and Mittlefehldt, 2003; Buchanan et al., 1993); see Figures 4 and 5. The points between regions #5 and #3 represent voxels that contain both carbonaceous chondrite and diogenitic pyroxene.

Figure 5. EET 87503,73 – Anaglyph of two NCT views (contrasts enhanced), separated by 8° view angle, for viewing with red-green glasses. The dark areas (high neutron attenuation, are CC fragments. The largest of them (top center) appears in Figure 4.

Figure 4 shows a fairly typical plane through the EET 87503,73 sample, with materials segmented according to Figure 3. The matrix shows no obvious structure (besides a little streaking that arises from the rotation of the tomography scan), which is consistent with observations that the meteorite lacks internal layering. The slice crosses one large angular fragment of hydrogen-bearing carbonaceous chondrite, in green. This fragment shows no internal structure (e.g., chondrules) suggesting that it could be CI- or CM-related, consistent with identification of CC fragments as CM-like (Buchanan and Mittlefehldt, 2003; Zolensky et al., 1996). The slice cuts through two eucrite fragments (higher Fe pyroxene, in purple); the irregular shape of the upper large eucritic pyroxene is consistent with it having a poikilitic texture (typical for pyroxene in basalt). The slice also shows several grains of Fe-Cr-Ti oxides (in orange), randomly distributed throughout the meteorite.

Figure 5 shows an anaglyph of neutron attenuation for the whole EET 87503 sample; the dark masses are nearly all hydrogen-bearing CC fragments, as the meteorite contains little metallic iron. From the anaglyph, one can see that the CC fragments are scattered randomly through the sample, and that most are angular. The anaglyph hints at some properties of the CC  that could be recovered by NCXT, for instance: size distribution, roundness/sphericity in relation to size, and spatial distribution, which can be analyzed quantitatively to describe the texture (cf. Anovitz et al., in submission). While one expects CC fragments in a breccia like this to be randomly distributed, other objects in other meteorites might show non-random distributions. SOM-3 contains a movie of EET 87503,73 rotating, in neutron attenuation.

### Aqueous Alteration: GRA 06100

GRA 06100 is a CR2 carbonaceous chondrite (Fig. 2b) – a type that contains abundant metal, and also abundant hydrogen as hydroxyl and bound water in minerals (Weisberg et al., 2006; Weisberg et al., 1993). As such, it provides a good demonstration of NXCT’s capabilities for visualizing and interpreting the distributions of Fe and H in primitive meteorites.

The bivariate histogram for GRA 06100,84 (Fig. 6) is for a subset of the original tomogram; the bivariate histogram of the full tomograms showed an extended field of points at X-ray attenuations near zero and neutron attenuations up to 20 (see SOM 1). These points all mapped to a single rounded object on the aluminum mesh that supported the sample. We interpreted this object as a fragment of plastic and cropped both tomograms to remove it. The bivariate histogram of Figure 6 and following figures are for the cropped tomograms.

The bivariate histogram for the cropped GRA 06100,84 tomogram (Fig. 6) shows fewer clearly defined fields than does the howardite histogram (Fig. 3). This paucity of clearly defined fields reflects the facts that the meteorite contains a wide variety of anhydrous particles (chondrules and rock fragment), contains abundant matrix with grain sizes much smaller than the voxel size of the tomograms, and has experienced variable degrees of aqueous alteration. The major concentration of points in region #3 is interpreted as magnesian silicate minerals (olivine and pyroxenes) in chondrules and matrix (see SOM 1 for details of the histographic segmentation regions). Region #3 grades into regions #4 and #5 by increasing neutron attenuation, and these are interpreted as mixtures of the anhydrous silicates of region #3 with hydrous material of greater neutron attenuation and similar X-ray attenuation. Region #6 appears distinct from the group of regions #3 – #5 in having both greater X-ray and neutron attenuations. Based on the attenuations and its association with iron metal, region #6 material is interpreted to be composed of iron oxy-hydroxides. Finally, the concentration of points at high attenuations, region #7, represents Fe-Ni metal – an abundant constituent of CR chondrites.

Figure 6. GRA 06100, 84.  Bivariate histograms of neutron versus X-ray attenuation. Colors (‘Sand’ palette) indicates abundances of voxels with that combination of neutron and X-ray attenuations. White circumscribed regions (#1 & #3) have the greatest number of voxels, see Fig. 3 for color palette. Negative values of attenuations are not physical, and represent both Poisson counting statistics and effects of flat-fielding. Numbered regions are: 1, void space, plagioclase feldspar & support material; 2, plastic substrate; 3, anhydrous Mg-rich silicates; 4, low-hydration magnesian material; 5, intermediate-hydration magnesian material; 6, hydrated ferroan material; and 7, Fe-rich metal. See Supplemental Material for other color palettes.

Figure 7. GRA 06100,84 – a slice of the X-ray tomogram, contrast enhanced, with phases segmented according to the bivariate histogram of Figure 6. Scale bar is 1 cm. The gray background is the X-ray tomogram, showing Mg-rich (Type-1) chondrules in black, more ferroan matrix in gray, and iron-rich material in light gray. Overlain with segmentation of Figure 6: pink - Fe-rich metal (region 7); green - low-hydration material (region 4); and blue - more hydrated material (region 5); and purple - Fe-rich hydrated material (region 6). Arrows denote largest areas of Fe-rich hydrated material. See Supplemental Materials for segmentation definitions on the bivariate attenuation histogram.

Figure 7 shows a plane section through the GRA 06100,84 tomogram; the gray background is X-ray attenuation, and the colored areas represent segments defined in Figure 6 (see SOM 1 for details). Metal (pink in Fig. 7) occurs mostly as spherical chondrules and as spherical shells in and around chondrules; Fe-rich hydrous material (purple in Figure 7) occurs near many (but not all) masses if Fe-metal.

Of more interest are the magnesian H-bearing materials, which appear on the bivariate histogram as a continuum from anhydrous silicates of region 3 to increasing neutron attenuations in regions 4 and 5. These regions likely represent mixtures of anhydrous silicates with serpentines and smectcite clays, as identified in petrographic studies (Abreu and Bullock, 2013; Abreu and Singletary, 2011; Abreu and Stanek, 2009). These materials are common in parts of the rock (e.g., upper and right sides of Fig. 7) and completely absent in others (Harju et al., 2014). The material richer in H (blue in Fig. 6), i.e. more aqueously altered, is always surrounded by less H-rich material (green in Fig. 6), suggesting that alteration was focused in certain areas, and spread out from them. This interpretation is consistent with the three-dimensional distribution of aqueously altered material; Figure 8 shows that the most aqueously altered material (in blue) is concentrated on planar surfaces in the meteorite. This pattern suggests that the alteration arose from fluid flowing along cracks, and penetrating from them into the surrounding, relatively porous, rock.

Figure 8. GRA 06100,84: XCT view (gray shading) with areas segmented as in Figure 6; oriented to show its planar concentrations of hydrated material. Scale bar is 1 cm. Areas of more hydrated material are blue (region 4, Figure 6); areas of iron metal are red (region 7). Hydrated material is concentrated along planar zones in the meteorite (arrows); outside these zones, the meteorite contains little hydrous material (i.e., it is minimally altered). See Supplemental Materials for segmentation definitions on the bivariate attenuation histogram.

SOM-4 contains a movie of GRA 06100,84 rotating, in neutron attenuation.

# Discussion

## Significance for Meteorite Studies

We have shown that coordinated X-ray and neutron tomography of meteorite samples can provide information that is unavailable by other means. The two methods together can image the interiors of meteorite samples, detect the presence of water-bearing (and chlorine-rich) materials, and delimit their distribution. Although we have focused on H-bearing materials, Cl-rich materials should also be detectable in NXCT, as Cl and H have similarly high neutron attenuation coefficients (Fig. 1). Alteration rinds on calcium-aluminum inclusions (CAIs) in chondrites commonly contain the Cl-rich mineral sodalite (Na4Al3Si3O12Cl), and should, therefore, be detectable by NXCT. Chlorine-rich apatite should also be detectable with NXCT, and this approach provide tests of hypotheses about its spatial distributions, e.g., Treiman et al. (2014) and Treiman and Irving (2008). It is also conceivable that NXCT could be used to detect locations and distributions of minerals rich in rare-earth elements (REE); some REE isotopes have elements have enormous neutron attenuations (Table 1).

With proper calibration and amenable samples, it should be possible to distinguish different varieties of carbonaceous chondrite fragments within a meteorite, based on the fragments’ neutron attenuations (i.e., proportions of hydrogen), metal, and chondrule abundances and sizes. The CM-like chondrite fragments in EETA 87503 contain no metal and few detectable chondrules; both are consistent with their CM classification. On the other hand, CI chondrites contain H2O equivalents of ~20% and few chondrules and CO3 chondrites contain ~0.3-3% H2O equivalents (Weisberg et al., 2006). These different H2O contents should be detectable in NCT, although data for EET 87503 show only one group (Fig. 3, area #5). Once identified by NCT, addition of XCT would allow estimation of the proportions and sizes of chondrules and metal, which should thereby allow classification to CC group (Weisberg et al., 2006).

Other meteorite breccias would also be good targets for coordinated NXCT – the more complex the breccia, the more useful NXCT could be. For example, the polymict ureilite meteorites, including Almahatta Sitta (Bischoff et al., 2010), contain clasts of a wide range of non-ureilitic material, including: carbonaceous chondrites, ordinary and Rumuriti chondrites, Fe-Ni metal, and plagioclase-rich achondrites (Beard et al., 2015; Boleaga and Goodrich, 2019; Boyle et al., 2017; Brearley, 1992; Goodrich et al., 2004; Goodrich et al., 2016; Goodrich et al., 2019a; Goodrich et al.; Kebukawa et al., 2019; Shaddad et al., 2010). The carbonaceous chondrite clasts, in particular, have significant implications for material distribution in the early solar nebula, and significant masses of them are needed for isotopic analysis (Yin et al., 2018). NXCT is an ideal tool for locating these clasts in situ. The ultimate meteorite breccia is Kaidun (MacPherson et al., 2009; Zolensky and Ivanov, 2003), which contains a bewildering array of chondritic and achondritic material (Ivanov et al., 2003; Ivanov et al., 1996; Ivanova et al., 2005; Zolensky et al., 1996). NXCT of such breccias would allow location and characterization of such and other significant clasts in situ, and facilitate identification, analyses, and conservation of these rare materials.

## Effects on Samples

### Neutron capture & transmutation

In neutron tomography, some neutrons will be captured by atomic nuclei in the sample creating neutron-richer isotopes, thus increasing their abundances and reducing the abundances of the neutron-capturing isotopes (Leya and Masarik, 2013). In tomography here, the samples experienced a thermal (E~25 meV) fluence of ~4x1011 neutron-cm-2. For comparison, typical neutron activation analyses involve neutron fluences of ~2x1016 to ~5x1018 cm2 , e.g. Kallemeyn (1993) and Korotev et al. (2009). From the low neutron fluences in tomography, one should expect minimal transformations into new isotopes or elements, but some high-precision isotopic analyses could be affected. Table 1 shows expected isotopic effects of neutron tomography on a rock of CI composition on those isotopes with the highest capture cross-sections. The most strongly affected isotope ratios would be changed by less than a part per million, which could still be significant for some analyses like cosmic ray exposure conditions and ages (Avila et al., 2016; Hidaka et al., 2020). A spreadsheet showing these calculations is available as SOM-5.

However, the importance of neutron capture effects during NCT must be considered for individual rock or mineral types. The most significant effect described in the literature of natural neutron fluence is on the halfnium-tungsten (Hf-W) chronometer system in lunar samples. Hf-W is an extinct chronometer, in which 182W (half-life of 9 million years) was created from 182Hf by the nuclear reaction 182Hf(-)182Ta(-)182W. Mineral or rock isochrons from Hf-W give the time of metal segregation (i.e., planetary core formation) relative to the formation of solids in the solar system (Kleine and Walker, 2017). However, the chronometer can be confounded by transmutation of 181Ta via 181Ta(n,g)182Ta(b-)182W, which can thus cause the chronometer to give anomalously old apparent ages (Lee et al., 2002; Leya and Masarik, 2013; Leya et al., 2000; Sprung et al., 2013). To estimate the effect of our neutron tomography on the Hf-W chronometer, we calculate the proportion of 181Ta that would be produced in a Ta-rich material, for which we take the ilmenite of lunar basalt Table 1. Most Significant Neutron Capture Effects from Neutron Tomography – CI Chondrite

| Isotope | Capture cross-section* | Isotope Ratio | Isotope Ratio Change |
| --- | --- | --- | --- |
|  |  |  | fraction | µ units† |
| 157Gd | 259000 | 158/157Gd | 2.24 x10-7 | 0.224 |
| 149Sm | 42080 | 150/149Sm | 3.64 x10-8 | 0.036 |
| 155Gd | 61100 | 156/155Gd | 2.64 x10-8 | 0.026 |
| 113Cd | 20600 | 114/113Cd | 1.78 x10-8 | 0.018 |
| 10B | 3835 | 11/10B | 3.31 x10-9 | 0.003 |
| 151Eu | 9100 | 153/151Eu | 2.50 X10-9 | 0.003 |
| 6Li | 940 | 7/6Li | 8.12 x10-10 | 0.001 |
| 50V | 60 | 50/51V | -2.39 x10-11 | 0.000 |
| 35Cl | 44.1 | 35/37Cl | -7.84 x 10-11 | 0.000 |
| 50Cr | 15.8 | 50/54Cr | -6.50 x10-12 | 0.000 |
| 53Cr | 18.1 | 53/54Cr | -4.60 x10-12 | 0.000 |
| 48Ti | 7.84 | 48/47Ti | -2.86 x10-12 | 0.000 |

* In barns, = 10-24 cm2 (Sears, 1992).

Calculated for a target of CI composition, elemental and isotopic (Lodders, 2021), and a thermal neutron fluence of 4.32x1011 cm-2 as used here (Treiman et al., 2018). Isotope ratio normalizes to an abundant isotope with a low capture cross-section, or the captured-neutron isotope.

† µ units are parts per million difference from the ratio of the isotope standard (ratio in CI meteorites unless otherwise specified (Lodders, 2021).

15555 (Lee et al., 2002). Lee et al. (2002) analyzed the ilmenite and other phases of 15555 for abundances of W and Ta and isotope ratios of W and Hf (nearly all Ta is 181Ta) and found that the rock had no evidence for natural production of 182W from 181Ta. Using the isotope ratios and element abundances of Lee et al. (2002), and taking the neutron absorption cross-section for 181Ta for the thermal neutrons used in NXCT (Sears, 1992), we find that NXCT as performed here would change the ilmenite’s 182W abundance by about one part in 10-8, and change the 182W/184W ratio by a few parts in 107, or ~0.003 e units, which is smaller than the ~0.1  units uncertainty in current 182W/184W analyses (Kruijer et al., 2017; Peters et al., 2021). Even so, we recommend that high-precision isotopic analyses avoid samples that have experienced neutron tomography.

### Residual Radioactivity

The neutron irradiation in coordinated tomography will produce some radioactivity in a sample, but the neutron fluence (as noted above) is far lower than for typical chemical analyses by neutron activation. For most natural samples, the most significant source of residual radioactivity is 24Na, which is produced by neutron capture on 23Na. The half-life of 24Na is 15 hours, so essentially all of its radioactivity will decay away in the first week after irradiation (>10 half-lives). In any case, all radiation facilities will retain samples subjected to tomography until their radioactivity levels are below Department of Transportation exempted quantity limits for shipping.

### Heating

Neutron and X-ray tomography are expected to cause minimal heating of the sample. Assuming that all the incident neutrons are absorbed by a sample, the NIST-NeXT system is estimated to deposit <1x10-6 Watt-cm-2 in the sample. Resultant heating of the sample will be insignificant for nearly every analysis, except those of the most volatile organic compounds.

### Thermoluminescence

Analysis of thermoluminescence, light emitted by a sample as it is heated, can provide information about the sample’s exposure to ionizing radiation in space and on Earth (Benoit et al., 1993; Benoit and Sears, 1997). These ionizing radiations can displace electrons from their normal sites to ‘traps’ elsewhere in the crystal structure; light is emitted as they return to their normal sites. Sears et al. (2018) have shown that X-ray computed tomography can overprint a sample’s natural thermoluminescence and destroy whatever information could have been garnered. This overprinting will certainly occur during NXCT, with the added complication that the neutron fluence will likely induce additional centers of luminescence. So, as Sears et al. (2018) note, one must be aware that a sample subjected to NXCT will lose memory of its thermoluminescence history of natural ionizing radiation.

## Conclusion

The results of this study have demonstrated the potential utility of NXCT imaging, not only for meteoritic materials, but also for a wide range of geologic and other samples (e.g. ceramics, steels, concretes etc.). These data both provide a guide to more specific sampling and direct determination of three-dimensional structures prior to more quantitative textural analysis (cf. Anovitz et al., in subm.).

While beyond the scope of this paper, several additional approaches may further enhance this technique. Ongoing efforts to improve the resolution and sensitivity of neutron imaging (Hussey et al., 2021; Trtik et al., 2015) will make the neutron data more comparable to those obtained using X-rays, and correlation and addition of results from neutron Bragg-edge imaging (Vitucci et al., 2018) may add a third variable, correlated with large crystal structure or potentially strain in the sample, to results from neutron and X-ray attenuation. In addition, the histogram-based segmentation techniques employed here, while sufficient for the purposes of this paper, can be enhanced to better separate the various phases involved, in part by taking advantage of their three-dimensional spatial associations, using one or more cluster analysis techniques (e.g. K-means, K-medians, mean-shift, density-based spatial clustering of applications with noise (DBSCAN), Expectation–Maximization (EM) Clustering using Gaussian Mixture Models (GMM), Agglomerative Hierarchical Clustering (HAC) etc.). Regardless of the approach used, or of future improvements or additions, however, it is clear from the results presented here that NXCT provides a highly useful approach to the three-dimensional imaging and analysis of many types of solid materials.

## Acknowledgments

We are grateful to the Meteorite Working Group (MWG) and the Antarctic Meteorite Curation Facility (ARES/JSC) for the loan of Antarctic (ANSMET) meteorite samples. Funding for the neutron and X-ray tomography was provided through the US Department of Commerce, NIST Physical Measurement Laboratory, and the Radiation Physics Division. Work by LMA was supported by the U.S. Department of Energy, Office of Science, Office of Basic Energy Sciences, Chemical Sciences, Geosciences, and Biosciences Division. License to use the Dragonfly© image processing program was courtesy of its developer, Object Research Systems (https://www.theobjects.com/company/index.html); the authors greatly appreciate ORS’ video training materials. Secret handshake to Jose Avila of USRA IT, who provided access to a computer capable of running the tomographic reconstructions. I. DeClue’s participation was via a NIST research internship (mentored by J. LaManna) while she was a student at Montgomery Blair High School, Silver Spring, Maryland. The Lunar and Planetary Institute (LPI) is operated by USRA, Universities Space Research Association, under a cooperative agreement with the Science Mission Directorate of NASA. We appreciate careful and thoughtful reviews by D. Ebel and I. Zel. Lunar and Planetary Institute Contribution #29xx.

REFERENCES

Abreu N. M. and Bullock E. S. (2013) Opaque assemblages in CR2 Graves Nunataks (GRA) 06100 as indicators of shock‐driven hydrothermal alteration in the CR chondrite parent body. Meteoritics & Planetary Science 48(12), 2406-2429.

Abreu N. M. and Singletary S. (2011) Alteration history of CR2 chondrite GRA 06100: FE-EPMA and TEM analysis. In Lunar and Planetary Science Conference 42nd, pp. Abstract 2659.

Abreu N. M. and Stanek G. (2009) Chemical and petrologic evidence of extensive and complex aqueous alteration of the CR GRA 06100. Lunar and Planetary Science Conference 40th 40, Abstract 2393.

Anovitz L., Cole D., Hussey D., LaManna J., Swift A., and Jacobson D. (2016) Combined neutron and X-Ray radiographic/tomographic analysis of dissolution of limestones under acidic conditions. AGU Fall Meeting Abstracts 2016, #H13F-1442.

Arnold J. R., Testa J. P., Friedman P. J., and Kambic G. X. (1983) Computed tomographic analysis of meteorite inclusions. Science 219(4583), 383-384.

Avila J., Ireland T., Lugaro M., Gyngard F., and Karakas A. (2016) Gadolinium and dysprosium isotopic compositions in stardust SiC grains from the Murchison meteorite. In 79th Annual Meeting of the Meteoritical Society, pp. 6318.

Beard A. D., Downes H., and Chaussidon M. (2015) Petrology of a nonindigenous microgranitic clast in polymict ureilite EET 87720: Evidence for formation of evolved melt on an unknown parent body. Meteoritics & Planetary Science 50(9), 1613-1623.

Benoit P. H., Jull A. J. T., McKeever S. W. S., and Sears D. W. G. (1993) The natural thermoluminescence of meteorites VI: Carbon‐14, thermoluminescence and the terrestrial ages of meteorites. Meteoritics 28(2), 196-203.

Benoit P. H. and Sears D. W. G. (1997) The orbits of meteorites from natural thermoluminescence. Icarus 125(2), 281-287.

Bischoff A., Horstmann M., Pack A., Laubenstein M., and Haberer S. (2010) Asteroid 2008 TC3—Almahata Sitta: A spectacular breccia containing many different ureilitic and chondritic lithologies. Meteoritics & Planetary Science 45(10‐11), 1638-1656.

Boleaga Y. and Goodrich C. (2019) Xenolithic Fe, Ni metal in polymict ureilite meteorites. In Lunar and Planetary Science Conference, pp. Abstract #1662.

Boyle S., Goodrich C., Kita N., Treiman A., and Gross J. (2017) Calcic plagioclase-rich clasts resembling the NWA 7325 ungrouped achondrite in polymict ureilites. In Lunar and Planetary Science Conference 48th, pp. Abstract #1219.

Brearley A. J. (1992) CI chondrite-like clasts in the Nilpena polymict ureilite: Implications for aqueous alteration processes in CI chondrites. Geochimica et Cosmochimica Acta 56(3), 1373-1386.

Briani G., Gounelle M., Bourot‐Denise M., and Zolensky M. E. (2012) Xenoliths and microxenoliths in H chondrites: Sampling the zodiacal cloud in the asteroid Main Belt. Meteoritics & Planetary Science 47(5), 880-902.

Briani G., Quirico E., Gounelle M., Paulhiac-Pison M., Montagnac G., Beck P., Orthous-Daunay F.-R., Bonal L., Jacquet E., and Kearsley A. (2013) Short duration thermal metamorphism in CR chondrites. Geochimica et Cosmochimica Acta 122, 267-279.

Buchanan P. C. and Mittlefehldt D. W. (2003) Lithic components in the paired howardites EET 87503 and EET 87513: Characterization of the regolith of 4 Vesta. Antarctic Meteorite Research 16, 128-151.

Buchanan P. C., Zolensky M. E., and Reid A. M. (1993) Carbonaceous chondrite clasts in the howardites Bholghati and EET87513. Meteoritics 28(5), 659-669.

Canella L., Kudějová P., Schulze R., Türler A., and Jolie J. (2009) PGAA, PGAI and NT with cold neutrons: Test measurement on a meteorite sample. Applied radiation and isotopes 67(12), 2070-2074.

Caporali S., Grazzi F., Salvemini F., Garbe U., Peetermans S., and Pratesi G. (2016) Structural characterization of iron meteorites through neutron tomography. Minerals 6(1), 14.

Caporali S., Pratesi G., Kabra S., and Grazzi F. (2018) Type I and type II residual stress in iron meteorites determined by neutron diffraction measurements. Planetary and Space Science 153, 72-78.

Carlson W. D. (2006) Three-dimensional imaging of earth and planetary materials. Earth and Planetary Science Letters 249(3-4), 133-147.

Cartwright J., Ott U., and Mittlefehldt D. (2014) The quest for regolithic howardites. Part 2: Surface origins highlighted by noble gases. Geochimica et Cosmochimica Acta 140, 488-508.

Cashman K. V. and Ferry J. M. (1988) Crystal size distribution (CSD) in rocks and the kinetics and dynamics of crystallization. Contributions to Mineralogy and Petrology 99(4), 401-415.

Charles C. R., Robin P. Y. F., Davis D. W., and McCausland P. J. (2018) Shapes of chondrules determined from the petrofabric of the CR 2 chondrite NWA 801. Meteoritics & Planetary Science 53(5), 935-951.

Chiaramonti A. N., Goguen J. D., and Garboczi E. J. (2017) Quantifying the 3-dimensional shape of lunar regolith particles using X-ray computed tomography and scanning electron microscopy at sub-µ resolution. Microscopy and Microanalysis 23(S1), 2194-2195.

Cooper G. and Rios A. C. (2016) Enantiomer excesses of rare and common sugar derivatives in carbonaceous meteorites. Proceedings of the National Academy of Sciences 113(24), E3322-E3331.

do Nascimento-Dias B., de Oliveira D., Machado A., Araújo O., Lopes R., and dos Anjos M. (2018) Utilization of nondestructive techniques for analysis of the Martian meteorite NWA 6963 and its implications for astrobiology. X‐Ray Spectrometry 47, 86-97.

DRAGONFLY (2021) Dragonfly version 2021.3, pp. software available at http://www.theobjects.com/dragonfly. Object Research Systems Inc., Montreal, Canada.

Duchnik S., Lanzky M., and Schmidt L. (2012) X-ray and Neutron Tomography of the Allende Meteorite. Københavns Universitet, Copenhagen, Denmark.

Ebel D., Fogel R., and Rivers M. (2005) Tomographic location of potential melt-bearing phenocrysts in lunar glass spherules. Lunar and Planetary Science XXXVI, Part 5.

Ebel D. S. and Rivers M. L. (2007) Meteorite 3‐D synchrotron microtomography: Methods and applications. Meteoritics & Planetary Science 42(9), 1627-1646.

Ebel D. S., Weisberg M. K., Hertz J., and Campbell A. J. (2008) Shape, metal abundance, chemistry, and origin of chondrules in the Renazzo (CR) chondrite. Meteoritics & Planetary Science 43(10), 1725-1740.

Eisenhour D. D. (1996) Determining chondrule size distributions from thin‐section measurements. Meteoritics & Planetary Science 31(2), 243-248.

Friedrich J. M. (2008) Quantitative methods for three-dimensional comparison and petrographic description of chondrites. Computers & Geosciences 34(12), 1926-1935.

Friedrich J. M. and Rivers M. L. (2013) Three-dimensional imaging of ordinary chondrite microporosity at 2.6 μm resolution. Geochimica et Cosmochimica Acta 116, 63-70.

Friedrich J. M., Weisberg M. K., and Rivers M. L. (2014) Multiple impact events recorded in the NWA 7298 H chondrite breccia and the dynamical evolution of an ordinary chondrite asteroid. Earth and Planetary Science Letters 394, 13-19.

Garenne A., Beck P., Montes-Hernandez G., Brissaud O., Schmitt B., Quirico E., Bonal L., Beck C., and Howard K. (2016) Bidirectional reflectance spectroscopy of carbonaceous chondrites: Implications for water quantification and primary composition. Icarus 264, 172-183.

Gnos E., Hofmann B., Franchi I., Al‐Kathiri A., Huser M., and Moser L. (2002) Sayh al Uhaymir 094: A new martian meteorite from the Oman desert. Meteoritics & Planetary Science 37(6), 835-854.

Goodrich C. A., Scott E. R., and Fioretti A. M. (2004) Ureilitic breccias: clues to the petrologic structure and impact disruption of the ureilite parent asteroid. Chemie der Erde-Geochemistry 64(4), 283-327.

Goodrich C. A., Treiman A. H., Kita N. T., and Defouilloy C. (2016) Increasing diversity of ordinary chondrite and Rumuruti-type chondrite clasts in polymict ureilites. In Lunar and Planetary Science Conference, pp. Abstract #1617.

Goodrich C. A., Zolensky M., Kohl I., Young E. D., Yin Q.-Z., Sanborn M. E., and Shaddad M. H. (2019a) Carbonaceous chondrite-like xenoliths in polymict ureilites: A large variety of unique outer solar system materials. In Lunar and Planetary Science Conference, pp. Abstract #1312.

Goodrich C. A., Zolensky M. E., Fioretti A. M., Shaddad M. H., Downes H., Hiroi T., Kohl I., Young E. D., Kita N. T., and Hamilton V. E. (2019b) The first samples from Almahata Sitta showing contacts between ureilitic and chondritic lithologies: Implications for the structure and composition of asteroid 2008 TC 3. Meteoritics & Planetary Science 54(11), 2769-2813.

Greshake A., Krot A. N., Meibom A., Weisberg M. K., Zolensky M. E., and Keil K. (2002) Heavily‐hydrated lithic clasts in CH chondrites and the related, metal‐rich chondrites Queen Alexandra Range 94411 and Hammadah al Hamra 237. Meteoritics & Planetary Science 37(2), 281-293.

Gross J., Eckley S., Zeigler R. A., and Vander Kaaden K. E. (2020) Treasure-trove Antarctica: Petrology, geochemistry, and pairing of lunar meteorites Dominion Range (DOM) 18509, 18543, and 18678. In 51st Lunar and Planetary Science Conference, pp. Abstract #2555. Lunar and Planetary Institute, Houston.

Hanna R. D. and Ketcham R. A. (2017) X-ray computed tomography of planetary materials: A primer and review of recent studies. Chemie der Erde-Geochemistry 77(4), 547-572.

Hanna R. D., Ketcham R. A., Zolensky M., and Behr W. M. (2015) Impact-induced brittle deformation, porosity loss, and aqueous alteration in the Murchison CM chondrite. Geochimica et Cosmochimica Acta 171, 256-282.

Harju E. R., Rubin A. E., Ahn I., Choi B.-G., Ziegler K., and Wasson J. T. (2014) Progressive aqueous alteration of CR carbonaceous chondrites. Geochimica et Cosmochimica Acta 139, 267-292.

Herrin J., Zolensky M., and Mittlefehldt D. (2010) A carbonaceous chondrite-rich lithology from the HED parent asteroid: PRA 04401. Meteoritics and Planetary Science Supplement 73, Abstract #5438.

Hess K.-U., Flaws A., Mühlbauer M., Schillinger B., Franz A., Schulz M., Calzada E., Dingwell D., and Bente K. (2011) Advances in high-resolution neutron computed tomography: Adapted to the earth sciences. Geosphere 7(6), 1294-1302.

Hezel D. C., Elangovan P., Viehmann S., Howard L., Abel R. L., and Armstrong R. (2013) Visualisation and quantification of CV chondrite petrography using micro-tomography. Geochimica et Cosmochimica Acta 116, 33-40.

Hicks L. J., Bridges J. C., and Gurman S. (2014) Ferric saponite and serpentine in the nakhlite martian meteorites. Geochimica et Cosmochimica Acta 136, 194-210.

Hidaka H., Mizutani Y., and Yoneda S. (2020) Estimation of Thermal and Epithermal Neutron Fluences at the Lunar Surface from Isotopic Compositions of Rare Earth Elements. The Astrophysical Journal 904(2), 183.

Howard K. T., Alexander C. M. O. D., Schrader D. L., and Dyl K. A. (2015) Classification of hydrous meteorites (CR, CM and C2 ungrouped) by phyllosilicate fraction: PSD-XRD modal mineralogy and planetesimal environments. Geochimica et Cosmochimica Acta 149, 206-222.

Hubbell J. H. and Seltzer S. M. (1996) Tables of X-Ray Mass Attenuation Coefficients and Mass Energy-Absorption Coefficients from 1 keV to 20 MeV for Elements Z = 1 to 92 and 48 Additional Substances of Dosimetric Interest In National Institute of Standards and Technology, Reference Database 126.

Humayun M., Nemchin A., Zanda B., Hewins R., Grange M., Kennedy A., Lorand J.-P., Göpel C., Fieni C., and Pont S. (2013) Origin and age of the earliest Martian crust from meteorite NWA 7533. Nature 503(7477), 513-516.

Hussey D. S., Abir M., Cook J. C., Jacobson D. L., LaManna J., Kilaru K., Ramsey B., and Khaykovich B. (2021) Design of a neutron microscope based on Wolter mirrors. Nuclear Instruments and Methods in Physics Research Section A: Accelerators, Spectrometers, Detectors and Associated Equipment 987, 164813.

Hussey D. S., LaManna J. M., Baltic E., and Jacobson D. L. (2017) Neutron imaging detector with 2 μm spatial resolution based on event reconstruction of neutron capture in gadolinium oxysulfide scintillators. Nuclear Instruments and Methods in Physics Research Section A: Accelerators, Spectrometers, Detectors and Associated Equipment 866, 9-12.

Ivanov A. V., Kononkova N. N., Yang S. V., and Zolensky M. E. (2003) The Kaidun meteorite: Clasts of alkaline‐rich fractionated materials. Meteoritics & Planetary Science 38(5), 725-737.

Ivanov A. V., MacPherson G. J., Zolensky M. E., Kononkova N. N., and Migdisova L. F. (1996) The Kaidun meteorite: Composition and origin of inclusions in the metal of an enstatite chondrite clast. Meteoritics & Planetary Science 31(5), 621-626.

Ivanova M. A., Kononkova N. N., and Ivanov A. V. (2005) First recorded find of ordinary chondrite material in the Kaidun meteorite. Solar System Research 39(2), 150-156.

Jenniskens P., Fries M. D., Yin Q.-Z., Zolensky M., Krot A. N., Sandford S. A., Sears D., Beauford R., Ebel D. S., and Friedrich J. M. (2012) Radar-enabled recovery of the Sutter’s Mill meteorite, a carbonaceous chondrite regolith breccia. Science 338(6114), 1583-1587.

Jolliff B., Yen C.-K., Gross J., Zeigler R., and Eckley S. (2021) Lithology of rock fragments in Apollo 17 double drive tube core 73002 using X-ray computed tomography and comparison to lithologic makeup of Station 3 soils. In Lunar and Planetary Science Conference 52nd, pp. Abstract #2681.

Joy K. H., Zolensky M. E., Nagashima K., Huss G. R., Ross D. K., McKay D. S., and Kring D. A. (2012) Direct detection of projectile relics from the end of the lunar basin–forming epoch. Science 336(6087), 1426-1429.

Kallemeyn G. W. (1993) Neutron Activation Analysis. In Advances in Analytical Geochemistry (eds. M. Hyman and M. W. Rowe), pp. 193-209. JAI Press, Inc.

Kaloyan A., Kovalenko E., Pakhnevich A., and Podurets K. (2017) The contrast scale of minerals for neutron tomography of paleontologic and geologic objects. Russian Geology and Geophysics 58(11), 1435-1440.

Kebukawa Y., Zolensky M. E., Ito M., Goodrich C. A., Marcus M. A., Kilcoyne A. L. D., Ohigashi T., Rahman Z., Shaddad M. H., and Kobayashi K. (2019) Investigation of organic matter in carbonaceous chondrite jlithologies of Almahata Sitta. In Lunar and Planetary Science Conference, pp. Abstract #1359.

Kichanov S. E., Kozlenko D. P., Kirillov A. K., Lukin E. V., Abdurakhimov B., Belozerova N. M., Rutkauskas A. V., Ivankina T. I., and Savenko B. N. (2019) A structural insight into the Chelyabinsk meteorite: Neutron diffraction, tomography and Raman spectroscopy study. SN Applied Sciences 1(12), 1563.

Kichanov S. E., Kozlenko D. P., Lukin E. V., Rutkauskas A. V., Krasavin E. A., Rozanov A. Y., and Savenko B. N. (2018) A neutron tomography study of the Seymchan pallasite. Meteoritics & Planetary Science 53(10), 2155-2164.

Kleine T. and Walker R. J. (2017) Tungsten isotopes in planets. Annual Review of Earth and Planetary Sciences 45, 389-417.

Korotev R. L., Zeigler R. A., Jolliff B. L., Irvin A. J., and Bunch T. E. (2009) Compositional and lithological diversity among brecciated lunar meteorites of intermediate iron concentration. Meteoritics & Planetary Science 44(9), 1287-1322.

Kruijer T. S., Kleine T., Borg L. E., Brennecka G. A., Irving A. J., Bischoff A., and Agee C. B. (2017) The early differentiation of Mars inferred from Hf–W chronometry. Earth and Planetary Science Letters 474, 345-354.

Krzesińska A. (2011) High resolution X-ray tomography as a tool for analysis of internal textures in meteorites. Meteorites 1, 3-12.

Krzesińska A. and Fritz J. (2014) Weakly shocked and deformed CM microxenoliths in the Pułtusk H chondrite. Meteoritics & Planetary Science 49(4), 595-610.

LaManna J., Chen J.-H., Althaus S., Liu Y., Hussey D., and Jacobson D. (2020a) Bivariate Histogram Segmentation of Simultaneous Neutron and X-ray Tomography for Improved Compositional and Structural Determination of Source Rock Shales. Microscopy and Microanalysis 26(S2), 3220-3221.

LaManna J., Hussey D., DiStefano V., Baltic E., and Jacobson D. (2020b) NIST NeXT: a system for truly simultaneous neutron and x-ray tomography. In Hard X-Ray, Gamma-Ray, and Neutron Detector Physics XXII, pp. 114940P. International Society for Optics and Photonics.

LaManna J. M., Hussey D. S., Baltic E., and Jacobson D. L. (2017) Neutron and X-ray Tomography (NeXT) system for simultaneous, dual modality tomography. Review of Scientific Instruments 88(11), 113702.

Lee D.-C., Halliday A. N., Leya I., Wieler R., and Wiechert U. (2002) Cosmogenic tungsten and the origin and earliest differentiation of the Moon. Earth and Planetary Science Letters 198(3-4), 267-274.

Lee M., Tomkinson T., Hallis L., and Mark D. (2015) Formation of iddingsite veins in the Martian crust by centripetal replacement of olivine: Evidence from the nakhlite meteorite Lafayette. Geochimica et Cosmochimica Acta 154, 49-65.

Leitner J., Hoppe P., and Zipfel J. (2011) The stardust inventory of the CR Chondrites GRA 95229 and GRA 06100 assessed by nanoSIMS. In Lunar and Planetary Science Conference, pp. Abstract #1713.

Leya I. and Masarik J. (2013) Thermal neutron capture effects in radioactive and stable nuclide systems. Meteoritics & planetary science 48(4), 665-685.

Leya I., Wieler R., and Halliday A. N. (2000) Cosmic-ray production of tungsten isotopes in lunar samples and meteorites and its implications for Hf–W cosmochemistry. Earth and Planetary Science Letters 175(1-2), 1-12.

Lodders K. (2021) Relative atomic solar system abundances, mass fractions, and atomic masses of the elements and their isotopes, composition of the solar photosphere, and compositions of the major chondritic meteorite groups. Space Science Reviews 217(3), 1-33.

MacPherson G. J., Mittlefehldt D. W., Lipschutz M. E., Clayton R. N., Bullock E. S., Ivanov A. V., Mayeda T. K., and Wang M.-S. (2009) The Kaidun chondrite breccia: Petrology, oxygen isotopes, and trace element abundances. Geochimica et Cosmochimica Acta 73(18), 5493-5511.

Martell J., Alwmark C., Holm-Alwmark S., Hall S., Hektor J., Woracek R., Helfen L., and Tengattini A. (2021) Neutron Tomography as a Tool for Pin-Pointing Meteoritic Components in Impactites. In Lunar and Planetary Science Conference 52nd, pp. Abstract #2086.

MATLAB (2021) MATLAB version 9.10.0.1613233 (R2021a). The Mathworks, Inc, , Natick, MA. pp. software available at https://www.mathworks.com/products/matlab.html.

Matsumoto T., Tsuchiyama A., Nakamura-Messenger K., Nakano T., Uesugi K., Takeuchi A., and Zolensky M. E. (2013) Three-dimensional observation and morphological analysis of organic nanoglobules in a carbonaceous chondrite using X-ray micro-tomography. Geochimica et Cosmochimica Acta 116, 84-95.

Mattes D., Haynor D. R., Vesselle H., Lewellyn T. K., and Eubank W. (2001) Nonrigid multimodality image registration. In Medical Imaging 2001: Image Processing, pp. 1609-1620. International Society for Optics and Photonics.

Mees F., Swennen R., Van Geet M., and Jacobs P. (2003) Applications of X-ray computed tomography in the geosciences. Geological Society, London, Special Publications 215(1), 1-6.

Mittlefehldt D. W. (2015) Asteroid (4) Vesta: I. The howardite-eucrite-diogenite (HED) clan of meteorites. Chemie der Erde-Geochemistry 75(2), 155-183.

Mittlefehldt D. W., Herrin J. S., Quinn J. E., Mertzman S. A., Cartwright J. A., Mertzman K. R., and Peng Z. X. (2013) Composition and petrology of HED polymict breccias: The regolith of (4) Vesta. Meteoritics & Planetary Science 48(11), 2105-2134.

Needham A. W., Abel R. L., Tomkinson T., and Grady M. M. (2013) Martian subsurface fluid pathways and 3D mineralogy of the Nakhla meteorite. Geochimica et Cosmochimica Acta 116, 96-110.

Needham A. W., Bilheux H. Z., Eckley S. A., and Zeigler R. A. (2020) Coordinated analyses of chondrites using neutron and X-ray computed tomography, and electron microscopy. In Lunar and Planetary Science Conference 51st, pp. Abstract #2179.

Pakhnevich A. (2016) On the application of tomography techniques to search for water and organic matter in meteorites. In Brucker microCT users meeting 2016, pp. 219-228.

Peetermans S., Grazzi F., Salvemini F., Lehmann E., Caporali S., and Pratesi G. (2013) Energy-selective neutron imaging for morphological and phase analysis of iron–nickel meteorites. Analyst 138(18), 5303-5308.

Perfect E., Cheng C.-L., Kang M., Bilheux H., Lamanna J., Gragg M., and Wright D. (2014) Neutron imaging of hydrogen-rich fluids in geomaterials and engineered porous media: A review. Earth-Science Reviews 129, 120-135.

Peters B. J., Mundl‐Petermeier A., Carlson R. W., Walker R. J., and Day J. M. (2021) Combined lithophile‐siderophile isotopic constraints on Hadean processes preserved in ocean island basalt sources. Geochemistry, Geophysics, Geosystems 22(3), e2020GC009479.

Riad R., Ibhi A., Douzi H., Elhajji M., Rozenbaum O., Harba R., and Jennane R. (2014) Investigation of the meteorites porosity by X-ray tomography and 3D image processing. In 2014 Second World Conference on Complex Systems (WCCS), pp. 710-714. IEEE.

Righter K. and Garber J. (2011) EETA 87503 and EET 87513. In The HED Compendium (eds. K. Righter and J. Garber). NASA Johnson Space Center, TX.

Robin P.-Y. F. and Charles C. R. (2015) Quantifying the three-dimensional shapes of spheroidal objects in rocks imaged by tomography. Journal of Structural Geology 77, 1-10.

Rubin A. E. and Bottke W. F. (2009) On the origin of shocked and unshocked CM clasts in H‐chondrite regolith breccias. Meteoritics & Planetary Science 44(5), 701-724.

Russ J. (1986) Practical Stereology. Plenum Press, New York, NY. pp. 185.

Ruzicka A., Brown R., Friedrich J., Hutson M., Hugo R., and Rivers M. (2015) Shock-induced mobilization of metal and sulfide in planetesimals: Evidence from the Buck Mountains 005 (L6 S4) dike-bearing chondrite. American Mineralogist 100(11-12), 2725-2738.

Sasso M. R., Macke R. J., Boesenberg J. S., Britt D. T., Rivers M. L., Ebel D. S., and Friedrich J. M. (2009) Incompletely compacted equilibrated ordinary chondrites. Meteoritics & planetary science 44(11), 1743-1753.

Schrader D. L., Connolly Jr H. C., Lauretta D. S., Nagashima K., Huss G. R., Davidson J., and Domanik K. J. (2013) The formation and alteration of the Renazzo-like carbonaceous chondrites II: Linking O-isotope composition and oxidation state of chondrule olivine. Geochimica et Cosmochimica Acta 101, 302-327.

Schrader D. L., Franchi I. A., Connolly Jr H. C., Greenwood R. C., Lauretta D. S., and Gibson J. M. (2011) The formation and alteration of the Renazzo-like carbonaceous chondrites I: Implications of bulk-oxygen isotopic composition. Geochimica et Cosmochimica Acta 75(1), 308-325.

Sears D. W., Sehlke A., Friedrich J. M., Rivers M. L., and Ebel D. S. (2018) X‐ray computed tomography of extraterrestrial rocks eradicates their natural radiation record and the information it contains. Meteoritics & Planetary Science 53(12), 2624-2631.

Sears V. F. (1992) Neutron scattering lengths and cross sections. Neutron news 3(3), 26-37.

Shaddad M. H., Jenniskens P., Numan D., Kudoda A. M., Elsir S., Riyad I. F., Ali A. E., Alameen M., Alameen N. M., and Eid O. (2010) The recovery of asteroid 2008 TC3. Meteoritics & Planetary Science 45(10‐11), 1557-1589.

Sprung P., Kleine T., and Scherer E. E. (2013) Isotopic evidence for chondritic Lu/Hf and Sm/Nd of the Moon. Earth and Planetary Science Letters 380, 77-87.

Tait A. W., Tomkins A. G., Godel B. M., Wilson S. A., and Hasalova P. (2014) Investigation of the H7 ordinary chondrite, Watson 012: Implications for recognition and classification of Type 7 meteorites. Geochimica et Cosmochimica Acta 134, 175-196.

Tomkinson T., Lee M. R., Mark D. F., Dobson K. J., and Franchi I. A. (2015) The Northwest Africa (NWA) 5790 meteorite: A mesostasis‐rich nakhlite with little or no Martian aqueous alteration. Meteoritics & Planetary Science 50(2), 287-304.

Treiman A. H., Barrett R. A., and Gooding J. L. (1993) Preterrestrial aqueous alteration of the Lafayette (SNC) meteorite. Meteoritics 28(1), 86-97.

Treiman A. H., Boyce J. W., Gross J., Guan Y., Eiler J. M., and Stolper E. M. (2014) Phosphate-halogen metasomatism of lunar granulite 79215: Impact-induced fractionation of volatiles and incompatible elements. American Mineralogist 99(10), 1860-1870.

Treiman A. H. and Coleff D. M. (2018) Lunar meteorite Northwest Africa (NWA) 11421: X-Ray tomography and preliminary petrology. Meteoritics and Planetary Science 53, Abstract #6329.

Treiman A. H. and Irving A. J. (2008) Petrology of martian meteorite Northwest Africa 998. Meteoritics & Planetary Science 43(5), 829-854.

Treiman A. H., LaManna J. M., Anovitz L. M., Hussey D. S., and Jacobson D. L. (2018) Neutron computed tomography of meteorites: Detecting hydrogen-bearing materials. Lunar and Planetary Science Conference 49, Abstract #1993.

Treiman A. H. and Semprich J. (2019) Dunite in iunar meteorite Northwest Africa 11421: Petrology and origin. Lunar and Planetary Science Conference 50, Abstract #1225.

Trtik P., Hovind J., Grünzweig C., Bollhalder A., Thominet V., David C., Kaestner A., and Lehmann E. H. (2015) Improving the spatial resolution of neutron imaging at paul scherrer institut–the neutron microscope project. Physics Procedia 69, 169-176.

Uesugi M., Uesugi K., and Oka M. (2010) Non-destructive observation of meteorite chips using quantitative analysis of optimized X-ray micro-computed tomography. Earth and Planetary Science Letters 299(3-4), 359-367.

Vitucci G., Minniti T., Di Martino D., Musa M., Gori L., Micieli D., Kockelmann W., Watanabe K., Tremsin A., and Gorini G. (2018) Energy-resolved neutron tomography of an unconventional cultured pearl at a pulsed spallation source using a microchannel plate camera. Microchemical Journal 137, 473-479.

Warren P. H. (2011) Stable isotopes and the noncarbonaceous derivation of ureilites, in common with nearly all differentiated planetary materials. Geochimica et Cosmochimica Acta 75(22), 6912-6926.

Weisberg M. K., McCoy T. J., and Krot A. N. (2006) Systematics and evaluation of meteorite classification. In Meteorites and the Early Solar System II (eds. D. S. Lauretta and H. Y. McSween Jr), pp. 19-52. University of Arizona Press, Tucson, Arizona

Weisberg M. K., Prinz M., Clayton R. N., and Mayeda T. K. (1993) The CR (Renazzo-type) carbonaceous chondrite group and its implications. Geochimica et Cosmochimica Acta 57(7), 1567-1586.

Winkler B. (2006) Applications of neutron radiography and neutron tomography. Reviews in Mineralogy and Geochemistry 63(1), 459-471.

Yin Q.-Z., Sanborn M. E., Goodrich C. A., Zolensky M., Fioretti A. M., Shaddad M., Kohl I. E., and Young E. D. (2018) Nebula scale mixing between non-carbonaceous and carbonaceous chondrite reservoirs: Testing the Grand Tack model with Almahata Sitta stones. In Lunar and Planetary Science Conference 49th.

Zeigler R. (2014) Nondestructive analysis of apollo samples by micro-CT and micro-XRF analysis: A PET style examination. Lunar and Planetary Science Conference 45th, Abstract #2665.

Zeigler R., Almeida N., Sykes D., and Smith C. (2017) Micro computed tomography and Micro X-ray fluorecence and tools for the curation and scientific study of Apollo samples. Proceedings NIPR Symposium on Antarctic Meteorites 40.

Zeigler R. A., Hanna R., Edey D., Ketcham R. A., Gross J., and McCubbin F. M. (2020) Using X-ray computed tomography to image Apollo drive tube 73002. In Lunar and Planetary Science Conference 51st, pp. Abstract #3023.

Zolensky M., Herrin J., Mikouchi T., Ohsumi K., Friedrich J., Steele A., Rumble D., Fries M., Sandford S., and Milam S. (2010) Mineralogy and petrography of the Almahata Sitta ureilite. Meteoritics & Planetary Science 45(10‐11), 1618-1637.

Zolensky M. and Ivanov A. (2003) The Kaidun microbreccia meteorite: A harvest from the inner and outer asteroid belt. Geochemistry 63(3), 185-246.

Zolensky M. E. (1997) Structural water in the Bench Crater chondrite returned from the Moon. Meteoritics & Planetary Science 32(1), 15-18.

Zolensky M. E., Weisberg M. K., Buchanan P. C., and Mittlefehldt D. W. (1996) Mineralogy of carbonaceous chondrite clasts in HED achondrites and the Moon. Meteoritics & Planetary Science 31(4), 518-537.

## Supplemental Online Materials

SOM 1: Supporting texts and figures.

- Tables of contents of SOMs.

- Table S1. Calculated and measured attenuation coefficients

C) Fig. S1. EET bivariate histogram with segmentation fields.

D) Fig. S2. EET bivariate histograms in different color palettes.

E) Fig. S3 Bivariate histogram for full GRA including weird blob.

F) Fig. S4 Bivariate histogram for cropped GRA in different color palettes.

G) Details of isotope effect calculations for Table 1, and of lunar ilmenite.

SOM 2: Zip archives of the NCT and XCT image slices, from which the 3-D tomograms were constructed.

SOM 3: Movie of EET 87503 rotating.

SOM 4: Movie of GRA 06100 rotating.

SOM 5. EXCEL Spreadsheet of isotope effect calculations for Table 1 of main text.

Trade names and company products are mentioned in the text or identified in illustrations in order to adequately specify the experimental procedure and equipment used. In no case does such identification imply recommendation or endorsement by the National Institute of Standards and Technology nor the Lunar and Planetary Institute, nor does it imply that the products are necessarily the best available for the purpose.